## Slide 1: Towards validating the runaway electron avalanche model in JOREK
E. Nardon
Acknowledgments: A. Järvinen, V. Bandaru, J. Artola, M. Hoelzl, D. Hu, M. Lehnen, C. Reux, N. Schwarz, C. Sommariva, C. Wang, the JOREK team and JET contributors
Runaway Electron Modelling Meeting, 10-14 June 2024

## Slide 2: !!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!! Warning: Work in progress Preliminary results !!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!

## Slide 3: Introduction
  Want to validate RE generation models, in particular here the avalanche model, using 2D simulations
    Here for JET #95135, where a RE beam was generated by an Ar MGI
  Problem:
    There are a number of ‘free’ input parameters
      E.g. RE seed current, Ar quantity in the plasma, …
    Can be used as knobs to fit the experimental data → Validation or ‘fancy fit’?
Γav x 0.5
True Γav
Γav x 2
  Possible solution: Show that if we falsify the model, the best possible fit to experimental data degrades
    Did this by hand last year [Nardon REM 2023]
    Started using Bayesian optimisation framework
    [Järvinen JPP 2022]
      Not shown today due to lack of time
      See [Nardon JOREK General Meeting, Feb. 2024] or backup slides
    Recently went back to do more tuning by hand
    …May go back to BO later 

## Slide 4: Outline
The experiment
Simulation setup
Simulation results
A look at synchrotron data
Issues
Summary and future work

## Slide 5: The experiment
1

## Slide 6: JET #95135
  A ‘famous pulse’ with benign RE termination [Reux PRL 2021]
  Target plasma: 3 T, 1.45 MA, Ohmic
  Ar MGI leads to a 0.65 MA RE beam
Ar
  (Note: t=0 is defined arbitrarily)

## Slide 7: Simulation setup
2

## Slide 8: Model
  JOREK reduced MHD model 600 with RE fluid (V. Bandaru)
  2D axisymmetric
  Free-boundary (JOREK-STARWALL) using ~realistic resistive wall + divertor support structures
  Evolve ψ, u (electric/flow potential), ρ, ρAr, T (single temperature), nRE
    Coronal equilibrium model for Ar
    No parallel flow
  No model for Ar gas dynamics
    → Cannot describe penetration of Ar into the plasma
    → Use ~homogeneous Ar source
  Prescribed RE seed
    No modelling of primary RE generation
    Here, used a radially broad Gaussian shape
  RE avalanche rate from [Hesslow JPP 2018, PPCF 2018]

## Slide 9: PF coils currents
  Initial currents:
    Exact experimental values would not give the right plasma position and shape
      No iron core in the model
      No induced currents in passive structures at t=0 in the model
    → Need adjustment to match EFIT equilibrium
    Start from exp. currents and fine-tune during Grad-Shafranov solver iterations
  Time evolution:
    Use same dIPF/dt as in exp. in all coils except for:
      Fast radial field coils, which are used for feedback on Zaxis, to match exp. value
      P4 (vertical field) coils, whose current is adjusted in some sims. to get a better match on Raxis
Fast radial field

## Slide 10: Simulation phases
  0) Equilibrium calculation
    Free-boundary Grad-Shafranov
  1) Initialisation of vertical stabilisation
  2) Ar injection
    Fast (50 µs) and broad (Gaussian of width 2 m, centered on magnetic axis)
  3) Thermal quench
    Large perpendicular heat conductivity
    Hyper-resistivity to flatten the j profile
  4) Current quench
    Keep injecting some Ar to match Ip decay rate

## Slide 11: Simulation results
3

## Slide 12: ‘Best match’ simulation
T12em6_Dpp1em6_MGICQ2p0e22_Zkpp1em5_reg0p75_rego0p0_regw10_Drei5em9_IP4adj500
  1.5·1020 Ar atoms in the plasma at start of RE plateau (19% Ar quantity in DMV)
  Avalanche gain ~ 100

## Slide 13: Progress since last year
JET95135_FB_PS_ZexpmFBinitGpm50Gdm2000_tshift48p0253_REjx4em3_MGI1d25u140_ZKperp1em3Ipspikeu3140_REadv1dm1Dpar1dm2_dtCQ50_n0
  ‘Best match’ as of Spring 2023
  ‘Best match’ now
  Main differences in settings (last year vs. now):
    RE perpendicular diffusivity DRE,perp: 3.2 vs. 0.016 m2/s → Avoids drop in plateau
    Te at boundary: 2 vs. 0.2 eV → Removes SOL (halo?) current
    Ar injection during CQ: no vs. yes → Maintains Ip match throughout CQ


## Slide 14
Current density
Argon density
Te
RE density
Max. 1.8 keV

## Slide 15
Current density
Argon density
Te
RE density
Max. 12 eV

## Slide 16
Current density
Argon density
Te
RE density
Max. 8.8 eV

## Slide 17
Current density
Argon density
Te
RE density
Max. 6.5 eV

## Slide 18
Current density
Argon density
Te
RE density
Max. 1.6 eV

## Slide 19
Current density
Argon density
Te
RE density
Max. 1.2 eV

## Slide 20
Current density
Argon density
Te
RE density
Max. 0.5 eV

## Slide 21
Current density
Argon density
Te
RE density
Max. 0.3 eV
Non-monotonic current profile develops during RE plateau. Also seen in ITER sims. [Bandaru NF 2024].
Reason? Link with Breizman’s theory [Breizman NF 2014]?

## Slide 22: Falsifying Γav: true / x 2 / x 0.5
T12em6_Dpp1em6_MGICQ2p0e22_Zkpp1em5_reg0p75_rego0p0_regw10_Drei5em9_IP4adj500
T12em6_Dpp1em6_MGICQ2p0e22_Zkpp1em5_reg0p75_rego0p0_regw10_Drei5em9_IP4adj500_avx2
T12em6_Dpp1em6_MGICQ2p0e22_Zkpp1em5_reg0p75_rego0p0_regw10_Drei5em9_IP4adj500_avo2
  Seed RE current is adjusted to match plateau level: 6.6 kA / 57 A / 61 kA
  True Γav looks better but not by a huge margin
    The difference was larger before [Nardon REM 2023] [Nardon JOREK GM 2024]

## Slide 23: A look at synchrotron data
4

## Slide 24
23 ms
18.5 ms
IR camera images vs. simulated RE density
  Exp. pattern initially localized at edge-bottom-HFS whereas simulated nRE peaked in the core
    Compatible? → To be assessed with JOREK synthetic synch. camera [Sommariva EPS 2023]
  Strong core peaking during plateau in exp. is not observed on simulated nRE
  Core peak suddenly disappears, likely due to a reconnection event
    Remindful of ASDEX Upgrade [Hoppe JPP 2021]
  Intensification of experimental emission over time
≈250
39.5 ms
≈1200
57.5 ms
≈2000

## Slide 25
  IR intensity lags behind nRE
  IR intensity keeps rising during RE plateau
    Likely due to pitch angle scattering, as in ASDEX Upgrade [Hoppe JPP 2021]
  More modelling (synthetic synch.) is needed to interpret this data and use it for validation
Space-integrated IR intensity
Gavx0.5
Gavx2
IR intensity vs. simulated IRE

## Slide 26: Issues
5

## Slide 27: Too small ne rise
  ne rise seems too small in sim. compared to interferometry data
    By a factor ~2 (to be confirmed)
  But a larger injected Ar quantity in the simulation would give a too fast Ip decay
  A matter of Ar profile? → Inject more Ar at the edge?
  D outgassing from the wall after TQ? → Inject D?

## Slide 28: Numerical instabilities
  Seem related to the coupled dynamics {REs ↔ electric/flow potential}
    jRE (= e·c·nRE) impacts ExB flow via ∇||j term in vorticity equation
    ExB flow impacts nRE via ExB advection
rego0p4w0p1f0p02_nsamp9.43e+24_MGIinCQ3e22_readv1dm1_Drepar0
  Instability tends to occur when using RE || advection, even at v||RE << c
  → Lately, I have been using v||RE=0, treating RE || transport as diffusive
    Even with pure diffusion, numerical instability appears when using a too *small* time step
Kinetic energy (A.U.)
Electric/flow potential
Time (ms)
9.3 ms
9.4 ms

## Slide 29: More technical issues
  Had to set a floor value (4 eV) for the Te used in the calculation of p*
    Otherwise p* calculation fails
  Had to kill the avalanche when ne < 5·1018/m3
    Otherwise may get very strong RE generation near LCFS at some point
  These ‘patches’ probably do not affect simulation results
  Needs investigation and discussion with JOREK colleagues

## Slide 30: Summary and future work
6

## Slide 31: Summary and future work
  Match to exp. Ip has improved and is now quite good
    Mainly as a result of reducing DRE,perp and removing SOL currents
    The inferred assimilated Ar quantity is plausible (~20% of total Ar)
  Looks like real validation and not a fancy fit: when falsifying Γav, the match in Ip degrades
    …Not by a lot though
  A non-monotonic current profile develops during RE plateau
    Reason to be investigated
  Future work:
    Compare with DREAM simulations by Aaro
    Model synchrotron radiation (Cristian)
    Exploit other data (interferometry, HXR monitor, fission chambers, …)
    Investigate issues
      Too small ne rise → Try D injection or more edge-peaked Ar injection
      Numerical issues → Investigate more and discuss with JOREK colleagues

## Slide 32: Backup slides

## Slide 33: ‘Best match’ simulation w/o adjusting P4 currents
T12em6_Dpp1em6_MGICQ2p0e22_Zkpp1em5_reg0p75_rego0p0_regw10_Drei5em9

## Slide 34: Flux loop data: exp. (plain) vs. sim. (dashed)
  Note that flux variation in the first 20 ms (≈CQ) is much larger at LCFS than at flux loops
FLRRU
FLRRL
FL05
FL11
FLD2
FLD3

## Slide 35: How much argon gets into the plasma?
  (Figure produced with M. Lehnen’s tool)
  Injection of 8·1020 Ar atoms from DMV 3
  Ar enters vessel over ~9 ms
  Ip spike only ~4 ms after gas arrival at plasma edge
  → At beginning of CQ, only ~23 % of the Ar has entered the vessel
  More Ar comes into the vessel during the CQ
    All Ar should be in vessel by the beginning of the RE plateau
  But how much of the Ar penetrates into the plasma?
    ~20%?
  (Note: t=0 is not the same in these 2 plots!)

## Slide 36: Argon quantity scan
NAr x 1.5
NAr x 1
NAr x 0.6
JET95135_FB_PS_ZexpmFBinitGpm50Gdm2000_tshift48p0253_REjx4em3_MGI1d25u210_ZKperp1em3Ipspikeu3140_REadv1dm1Dpar1dm2_dtCQ50_n0
JET95135_FB_PS_ZexpmFBinitGpm50Gdm2000_tshift48p0253_REjx4em3_MGI1d25u90_ZKperp1em3Ipspikeu3140_REadv1dm1Dpar1dm2_dtCQ50_n0

## Slide 37: Effect of RE seed shape
JET95135_FB_PS_ZexpmFBinitGpm50Gdm2000_tshift48p0253_REjx4em3_MGI1d25u140_ZKperp1em3Ipspikeu3140_REadv1dm1Dpar1dm2_dtCQ50_n0
JET95135_FB_PS_ZexpmFBinitGpm50Gdm2000_tshift48p0253_REgauss_MGI1d25u140_ZKperp1em3Ipspikeu3140_REadv1dm1Dpar1dm2_dtCQ50_n0
jREseed = αREseed j0
Homogeneous seed (level adjusted to match plateau value)
Avalanche gain: 120 vs 53

## Slide 38: Fixed- vs. free-boundary with realistic or ideal wall
JET95135_FixedB_tshift48p0253_REjx4em3_MGI1d25u140_ZKperp1em3Ipspikeu3140_REadv1dm1Dpar1dm2_dtCQ50_n0
JET95135_FB_PS_ZexpmFBinitGpm50Gdm2000_tshift48p0253_REjx4em3_MGI1d25u90_ZKperp1em3Ipspikeu3140_REadv1dm1Dpar1dm2_dtCQ50_n0
JET95135_FB_PS_ZexpmFBinitGpm50Gdm2000_tshift48p0253_REjx4em3_MGI1d25u90_ZKperp1em3Ipspikeu3140_REadv1dm1Dpar1dm2_dtCQ50_wrf1em6_n0
(Kept the same seed)

## Slide 39: Introduction to Bayesian approach for validation
  Explained in [Järvinen JPP 2022], where the approach is presented as a way to identify uncertain input parameters given observed experimental measurements
  Here, we use it in another way: validate a model by showing that the best match to experimental data degrades when ‘falsifying’ the model
  General idea: run sims. with different values of input parameters to try and maximize an objective function
  A standard BO algorithm consists of 2 main components:
    (i) A probabilistic model for the objective function
  = Low evaluation cost surrogate model for the objective function
      Here, use Gaussian Process regression with the Python GP framework
  (ii) An acquisition function for recommending the next sampling point(s)
      Uses the mean and variance of the probabilistic model to balance exploitation and exploration
        Here, use qExpectedImprovement
        Parallel acquisition of several samples (5 here)
  BO algorithm = Loop: collect samples, update probabilistic model, collect samples, …

## Slide 40: Example
  DREAM simulations of RE generation in JET 95135 (i.e. the same case that we are studying here)
  Simple example: try to guess Te during the CQ
    Only 1 input parameter to optimize
[Järvinen JPP 2022]

## Slide 41: Setting up the BO framework for our study
  Input:
    TQ transport coefficients (χ┴, ηh)
    Ar quantity
    Size of RE seed
  Output:
    Ip spike timescale
    Ip decay during CQ
    IRE plateau value
  → Not so hard to optimise by hand, but Bayesian optimisation is more convenient and objective
  Here, we will ask the BO framework to optimise 2 input parameters:
    Ar quantity
    Size of the RE seed
  Could add more in the future, e.g. RE seed spatial shape
  Objective function: -log(∫|Ip,sim-Ip,exp|dt)
    (time integral from Ip spike until 40 ms later)
~
  Note: There is a quite direct 1-to-1 relation between some input parameters and some output quantities:

## Slide 42: If you are curious…
  The files are on Marconi: /marconi_work/FUA37_REDIS/enardon0/JET95135_RE_generation_BO
  Python script = botorch_jorek_test.py
    Uses Python BO libraries
    Iterates the following loop:
      surrogate_model_steup: Updates probabilistic model based on result_dictionary
      acquire_candidates: Generates a batch of candidate values of input_params
      execute_batch: Creates associated simulation folders and files in run_folder, launches simulations, once finished calculates objective function
      append_result_dictionary: Updates result_dictionary

## Slide 43: Preliminary results: true Γav
Acquisition function keeps generating candidates in region where simulations fail, maybe because it thinks the objective function is large there
Failed simulations: don’t reach 40 ms (need to investigate why but probably related to Ip going down too fast)
Value of objective
function at simulated points
Order in which simulations have been run
Surrogate model for objective function
Initial RE current fraction
Initial RE current fraction
Initial RE current fraction
Ar quantity (A.U.)
Ar quantity (A.U.)
Ar quantity (A.U.)
New candidates
Best sim.: -18.13

## Slide 44: Preliminary results: Γav x 2
Initial RE current fraction
Initial RE current fraction
Initial RE current fraction
Ar quantity (A.U.)
Ar quantity (A.U.)
Ar quantity (A.U.)
Best sim.: -19.15
New candidates
Failed simulations: don’t reach 40 ms (need to investigate why but probably related to Ip going down too fast)
  NB: Changed range of initial RE current fraction to smaller values, consistently with stronger avalanche
Value of objective
function at simulated points
Order in which simulations have been run
Surrogate model for objective function

## Slide 45: Preliminary results: Γav x 0.5
Initial RE current fraction
Initial RE current fraction
Initial RE current fraction
Ar quantity (A.U.)
Ar quantity (A.U.)
Ar quantity (A.U.)
  NB: Changed range of initial RE current fraction to larger values, consistently with weaker avalanche
Best sim.: -18.51
New candidates
Failed simulations: don’t reach 40 ms (need to investigate why but probably related to Ip going down too fast)
Value of objective
function at simulated points
Order in which simulations have been run
Surrogate model for objective function