## Slide 1: Benign termination of runaway electron beams at JET: Radiated power and bolometry during massive material injections
N. Schoonheere, C. Reux, H. Meister, P. Carvalho, I. Coffey, K. Lawson, P. Puglia, U. Sheikh, JET contributors, and the EUROfusion Tokamak Exploitation Team

## Slide 2: Outline
The benign termination scheme
Spectroscopy study of mitigated runaway beams
Bolometry measurements after large gas injections
Conclusions and perspectives

## Slide 3: Benign termination scenario
1
2
Argon injection to trigger a disruption and RE beam
D2 (or H2) injection with standard gas valve, MGI or SPI
Recombination of the companion plasma
Final collapse: Large MHD instability + absence of regeneration  benign termination Demonstrated on JET, TCV, DIII-D and AUG
4
3
Companion plasma
JPN 95135
Notes: Show RE beam Ip
Explain companion plasma

## Slide 4: Benign termination – Operational limits
Experimental observations:
Condition for benign termination:
  Recombination of the companion plasma and stays recombined
Minimum amount of deuterium
  Neutral D2 provide heat transport to the walls
Maximum amount of argon or deuterium
  Makes the companion plasma more resistive
Balance between runaway interaction with the companion plasma and energy loss mechanisms
The composition and power balance of the companion plasma matters!

## Slide 5: Benign termination – radiated power
Ar trigger
D2 injection
Before D2:
Cold companion plasma ~12 eV [1]
After D2 :
Recombined
We expect the radiated power to go down
But..
Several megawatts of radiated power measured
[1] S.Sridhar, PhD thesis, 2020
JPN 95135

## Slide 6: Outline
The benign termination scheme
Spectroscopy study of mitigated runaway beams
Bolometry measurements after large gas injections
Conclusions and perspectives

## Slide 7: JET diagnostics – spectrum coverage
Objective:
Find the origin of this radiated power
Lyman
 α
Balmer
 α
Conclusions:
Some gaps remain but no obvious mechanism would explain the power in these ranges
Difference between the two UV detectors: Only the Lyman α
Bolometer
SXR
SXR
UV
spectrometer
UV diamond det.
Visible
spectrometer
X
X
X
?
X
Observations after D2 injection:
Gap
Gap
Notes: Can be from diamond detector (with Lyman alpha, carrying most of the energy)

## Slide 8: Opacity and the Lyman α
↑ Balmer α | Lyman  stay constant
both originate from n=3
These two lines should follow the same evolution
Strong opacity of the Lyman series from neutral D2
Postulate to explain the diamond detector signal:
The Lyman α (carries most of the energy) is also absorbed by the neutral D but can only be re-emitted as a Lyman α and can eventually exit the neutral gas after a number of absorptions-emissions
Balmer α (visible)
Lyman  (UV)
Notes: Lyman alpha carries the most energy

## Slide 9: Estimate of the D radiated power
Neutral density inside RE beam estimated with the power balance:
D cooling rates from the ADAS database
Electron density = 1018 m-3 (measurement floor)
Total radiated power for all D lines
Conclusions
D thermal radiation power is negligible at these temperatures
But doesn’t rule out non thermal radiation from RE interactions
Temperature for recombined D2 ~ 1eV [1]
[1] E. Hollmann et al, POP (2020)
Notes: Electron density: interferometer floor

## Slide 10: Outline
The benign termination scheme
Spectroscopy study of mitigated runaway beams
Bolometry measurements after large gas injections
Conclusions and perspectives

## Slide 11: Radiated power measured in empty vessel
No plasma
No radiation expected
Signal interpreted as several megawatts of radiated power
Correlated with neutral pressure
Radiated power [MW]
Pressure [Pa]
Massive D2 gas injection (MGI) into the empty vacuum vessel

## Slide 12: Resistive bolometers
Radiation incident on measurement absorber.
The temperature difference between measurement and reference sensor shielded from radiation is measured with thermistors in a Wheatstone bridge
Measured voltage ∆U interpreted as radiated power
Calibrated constants:
: cooling time [ ms ]
: Sensitivity [ V/W ]

## Slide 13: Effect of neutral gas pressure
Conduction through the gas affects the thermal dynamics of the bolometer sensors
Thermal conductivity model (developed with the help of H. Meister [1])
Power balance of the sensor :
    Different geometry  different cooling efficiency
Long conduction length
Short conduction length
[1] H.Meister et al, submitted to RSI (2024)

## Slide 14: Cooling times
Difference in cooling times between the measurement and reference sensors
The changing cooling time affects the calculated incident radiated power
But doesn’t explain the measured power in the absence of radiation
Nominal pressures
Pressures after injection

## Slide 15: Equilibrium temperatures
Joule heating power from the excitation voltage of the Wheatstone bridge (40 V P2P)
Measured voltage = measured radiated power
Different equilibrium temperature
Temperature [°c]
Nominal pressures
Pressures after injection
Nominal pressures
Pressures after injection

## Slide 16: Modelled channel power
A bridge imbalance and measured voltage arises following the increase in neutral pressure
The « incident power » on the sensor is calculated with the code used to process bolometry measurements
Good quantitative agreement with some channels, qualitative for others
Radiated power [MW m-2]
Pressure [Pa]
Voltage [mV]

## Slide 17: Total radiated power
We assume that all channels experience the same modelled voltage dependence
Total radiated power calculated from all channels using the algorithm used on JET real data (weighted sum of all channels)
Good reproduction of the time evolution

## Slide 18: Total radiated power peak
The model captures the difference between D2 and N2 ,due to their respective cooling efficiencies, but to a lesser degree
The saturation effect at higher pressure for D2 is not reproduced
Within the same order of magnitude as the measured radiated power

## Slide 19: Outline
The benign termination scheme
Spectroscopy study of mitigated runaway beams
Bolometry measurements after large gas injections
Conclusions and perspectives

## Slide 20: Conclusions and perspectives
The rise in radiated power cannot be due to thermal radiation
Unlikely to be due to UV deuterium lines due to strong opacity
Spurious radiated power at neutral pressures > 0.1 Pa up to several megawatts!
Represents the majority of the signal in runaway electron mitigation experiments
The magnitude of the effect depends on the gas species due to their individual cooling efficiencies
The change in calibrated constants can affect the calculated incident radiated power
Radiated power increase also for SPI in empty vessel
Radiation asymmetries: Vertical and horizontal bolometer cameras are affected differently

## Slide 21: D2 injection into RE beam
D2 massive gas injection @ 48.044s
Reionisation event @ 48.125s
Notes: We see an increase in the radiated power
Crashes on the limiter
No hotspots visible

## Slide 22: Backup : Power balance
Equating the power gain to the REs accelerated by the electric field to the power loss through collisions, Bremsstrahlung tabulated in the ESTAR database and synchrotron radiation
ESTAR:
Collision stopping power
Radiative stopping power: Bremsstrahlung
Assumptions:
Homogeneous neutral density inside RE beam
Mono-energetic RE population at 10 MeV
Ar : D2 ratio equal to ratio of initial quantities injected
No RE losses to the wall
Solve for deuterium density
Objective:
Estimate the radiated power emitted by D line radiation inside a RE beam using Photo emissivity coefficients (PEC)
But the D2 density inside the RE beam is unknown

## Slide 23: Backup : Deuterium

## Slide 24: Backup: Lyman alpha
The suspicion was that the Lyman alpha could be absorbed by the neutral deuterium but could escape as it can only be re-emitted as a Lyman alpha.
However, a spectroscopy measurement available for a single pulse shows the Lyman alpha decreasing
Not responsible for the radiated power
No conclusion for the signal increase of the diamond UV detector

## Slide 25: Backup : Comparing dry runs and real pulses
The dependence on the amount of deuterium injected in dry runs matches what we observe in runway beams.
The magnitude is also comparable.
Some radiation appears to remain in real pulses
We want to be able to recover the “real” radiated power
Mean radiated power measured 0.17s after SPI / MGI arrival.
RE pulses:
High Ar content

## Slide 26: Backup : Neutral pressure dependence
Cryopumps are responsible for the majority of the pumping on JET
When turned off, the “radiated power” takes a longer time to decrease
The bolometer response follows the neutral gas pressure evolution
D2 MGIs into the empty vacuum vessel with cryopumps on and off

## Slide 27: Backup: Injection location

## Slide 28: Backup : Peak radiated power after MGI
Spurious radiated power measured at neutral pressures > 0.1 Pa
Dependent on:
Quantity of gas injected
Gas species
Peak “radiated power” dependence on peak neutral pressure reached after massive gas injection (MGI)

## Slide 29: SPI into dry runs

## Slide 30: Backup : bridge voltage
VRMS = 14.14 V

## Slide 31: Backup: bolometer equations

## Slide 32: Backup : Model equations
Conductivity through solids:
Conductivity through gas:

## Slide 33: Backup : cooling time constant

## Slide 34: Backup : Pressure estimate
Saturation of the Penning gauges on JET at high pressures (> 1 Pa)
Dependent on gas species measured
Pumping model:
FR : Flow rate (injection) = 0 Pa m3 s-1
s : Pumping rate (D2) [1] = 200 m3 s-1
V : Vessel volume = 185 m3
Instantaneous gas dispersion
Isothermal expansion
Neutral pressure after MGI
[1] W. Obert, Proceedings of 16th International Symposium on Fusion Engineering, 1995
A fairly good match is obtained with penning gauges measurements

## Slide 35: Backup : Modelled channel power
A bridge imbalance and measured voltage arises following the increase in neutral pressure
The « incident power » on the sensor is calculated with the code used to process bolometry measurements
Good quantitative agreement with some channels, qualitative for others
Radiated power [MW m-2]
Pressure [Pa]
Voltage [mV]

## Slide 36: Backup : Channel responses
Lines of sight - vertical bolometer camera
Normalised peak voltage measured across channels D2 pulses:
Large discrepancies between channels
Adjacent channels can have very different responses: Not just caused by gas propagation effects
Depends on the channel’s individual characteristics
Bolometer head 4 channels
Bolometer camera:

## Slide 37: Backup : Why do we see such large variations?
The cooling time constantsof each channel is determined (in vacuum) by thermal conductivity of the:
  Thermal contact layer
  Mica substrate
Variations in thermal conductivity arise due to manufacturing tolerances and ageing of the materials
Calibrated cooling times: 123 – 252 ms !
These can also vary between the measurement and reference absorber
The temperature coefficient of resistivity can also vary between each resistor
Difficult to model exactly without experimental measurements!

## Slide 38: Backup : Peak channel voltage
Average peak voltage reached after MGI
Error bars show the minimum and maximum voltage across all channels
Modelled voltage within the same order of magnitude as the experimental results
But very large error bars, particularly at high pressures!

## Slide 39: Backup: parameter study