## Slide 1
R. Hellinga, T. A. Wijkamp, J. Decker, M. Hoppe, U. Sheikh, R. J. E. Jaspers,
the TCV team(a) and the EUROfusion Tokamak Exploitation Team(b)
(a) See the author list of H. Reimerdes et al., Nuclear Fusion 62 (4): 042018, 2022. DOI: 10.1088/1741-4326/ac369b
(b) See the author list of E. H. Joffrin et al., Nuclear Fusion, 2024. DOI: 10.1088/1741-4326/ad2be4
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
Runaway Electron Modelling Conference – June 2024
epfl.ch/about/overview/history-of-epfl/

## Slide 2: Introduction
The goal of this work is to investigate …
      (i) … the influence of the ECRH location (and power) on the effectiveness of the ECRH-induced expulsion of REs;
      (ii) … the evolution of the (radial) RE distribution to get more insights in the influence of the ECRH-induced expulsion on the RE transport.
Today, I will discuss the preliminary results on …
    (i) … the influence of the ECRH location on the hard X-ray emission;
    (ii) … the influence of the ECRH location on the synchrotron radiation power and the (radial) RE distribution.
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 1]
Notes: Even kijken naar verwoording punten

## Slide 3: Table of Contents
ECRH-induced expulsion of REs (model)
    Short recap of the zero-dimensional ECRH-induced expulsion of REs model;
    Analysis of the hard X-ray emission for different ECRH deposition locations;
Synchrotron radiation
    Introduction to the MANTIS system(s);
    Analysis of the synchrotron radiation power for different ECRH deposition locations;
    Introduction to SOFT and the tomographic inversion tool(s);
    Analysis of the tomographic inversions of the RE-distribution(s);
Outlook
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 2]

## Slide 4: Zero-dimensional ECRH-induced RE expulsion model
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 3a]
J. Decker et al. Expulsion of runaway electrons using ECRH in the TCV tokamak. arXiv, 2024. DOI: 10.48550/arXiv.2404.09900.
Time evolution of the population of REs is a balancing act between the generation of REs and the losses of REs.
Generation of REs:
    Dreicer generation rate ;
    Avalanche generation rate
    with avalanche generation rate coefficient .
Losses of runaway electrons:
    Loss rate with loss coefficient ;
  Analytical expression of the steady-state RE density can be derived from the balancing act (also known as the rate equation).

## Slide 5: Zero-dimensional ECRH-induced RE expulsion model
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 3b - Hidden]
J. Decker et al. Expulsion of runaway electrons using ECRH in the TCV tokamak. arXiv, 2024. DOI: 10.48550/arXiv.2404.09900.

## Slide 6: Zero-dimensional ECRH-induced RE expulsion model
How to ‘leave’ the high runaway electron current regime?
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 3c - Hidden]
J. Decker et al. Expulsion of runaway electrons using ECRH in the TCV tokamak. arXiv, 2024. DOI: 10.48550/arXiv.2404.09900.

## Slide 7: Zero-dimensional ECRH-induced RE expulsion model
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 4]
coefficient of REs
J. Decker et al. Expulsion of runaway electrons using ECRH in the TCV tokamak. arXiv, 2024. DOI: 10.48550/arXiv.2404.09900.

## Slide 8: Table of Contents
ECRH-induced expulsion of REs (model)
    Short recap of the zero-dimensional ECRH-induced expulsion of REs model;
    Analysis of the hard X-ray emission for different ECRH deposition locations;
Synchrotron radiation
    Introduction to the MANTIS system(s);
    Analysis of the synchrotron radiation power for different ECRH deposition locations;
    Introduction to SOFT and the tomographic inversion tool(s);
    Analysis of the tomographic inversions of the RE-distribution(s);
Outlook
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 2]

## Slide 9: ECRH-induced expulsion of REs – Shot overview
() |  |  |  |  |  | 
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 5]

## Slide 10: Analysis of the hard X-ray emission (PMTX signals)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 6]

## Slide 11: Analysis of the hard X-ray emission (PMTX signals)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 7]

## Slide 12: Analysis of the hard X-ray emission (PMTX signals)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 8]

## Slide 13: Analysis of the hard X-ray emission (PMTX signals)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 9]

## Slide 14: Analysis of the hard X-ray emission (PMTX signals)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 10a]
00 kW

## Slide 15: Analysis of the hard X-ray emission (PMTX signals)
 |  |  |  |  | 1421.30
 |  |  |  |  | 1417.33
 |  |  |  |  | 1416.46
 |  |  |  |  | 1421.30
 |  |  |  |  | 1417.33
 |  |  |  |  | 1416.46
 | 00 | 325 | 1.65 | 4
 | 00 | 325 | 1.70 | 4
 | 00 | 500 | 1.60 | 7
 |  | 325 | 1.65 | 4
 |  | 325 | 1.70 | 4
 |  | 500 | 1.60 | 7
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 10b - Hidden]

## Slide 16: Analysis of the hard X-ray emission (PMTX signals)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 11a]
00 kW

## Slide 17: Analysis of the hard X-ray emission (PMTX signals)
 |  |  |  |  | 1411.7
 |  |  |  |  | 141.4
 | 00 | 215 | 1.90 | 2
 | 00 | 350 | 1.65 | 4
 |  | 215 | 1.90 | 2
 |  | 350 | 1.65 | 4
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 11b - Hidden]

## Slide 18: Analysis of the hard X-ray emission (PMTX signals)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 12]
The effective loss coefficient, , becomes smaller if the ECRH power is deposited more radially outwards;
The relative increase of the loss coefficient becomes smaller if the ECRH power is deposited more radially outwards;
The relative decrease of the population of runaway electrons becomes smaller if the ECRH power is deposited more radially outwards;

## Slide 19: Table of Contents
ECRH-induced expulsion of REs (model)
    Short recap of the zero-dimensional ECRH-induced expulsion of REs model;
    Analysis of the hard X-ray emission for different ECRH deposition locations;
Synchrotron radiation
    Introduction to the MANTIS system(s);
    Analysis of the synchrotron radiation power for different ECRH deposition locations;
    Introduction to the tomographic inversion tool(s);
    Analysis of the tomographic inversions of the RE-distribution(s);
Outlook
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 2]

## Slide 20: Multispectral Advanced Narrowband Tokamak Imaging System
differ.nl/research/plasma-edge-physics-and-diagnostics/
Electron Cyclotron Resonance Heating as a mitigation strategy for runaway electrons
[Page 3]
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 13]
A. Perek et al. MANTIS: A real-time quantitative multispectral imaging system for fusion plasmas. Review of Scientific Instruments, 90 (12): 123514, 2019. DOI: 10.1063/1.5115569.

## Slide 21
Electron Cyclotron Resonance Heating as a mitigation strategy for runaway electrons
[Page 3]
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 14]
T. A. Wijkamp et al. Resonant interaction between runaway electrons and the toroidal magnetic field ripple in TCV.
Nuclear Fusion, 64 (1):016021, 2023. DOI: 10.1088/1741-4326/ad0dd7.
Top-port view
(MANTIS II-b)

## Slide 22: Multispectral Advanced Narrowband Tokamak Imaging System
Electron Cyclotron Resonance Heating as a mitigation strategy for runaway electrons
[Page 4]
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 15]
A. Perek et al. MANTIS: A real-time quantitative multispectral imaging system for fusion plasmas. Review of Scientific Instruments, 90 (12): 123514, 2019. DOI: 10.1063/1.5115569.
Personal collection

## Slide 23: Table of Contents
ECRH-induced expulsion of REs (model)
    Short recap of the zero-dimensional ECRH-induced expulsion of REs model;
    Analysis of the hard X-ray emission for different ECRH deposition locations;
Synchrotron radiation
    Introduction to the MANTIS system(s);
    Analysis of the synchrotron radiation power for different ECRH deposition locations;
    Introduction to the tomographic inversion tool(s);
    Analysis of the tomographic inversions of the RE-distribution(s);
Outlook
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 2]

## Slide 24
Resonant interaction(s) between REs and the toroidal magnetic field ripple:
    Scattering of REs towards large(r) pitch-angles (resulting in RE vortex);
    Significant contribution to synchrotron radiation power;
  Resonant momentum:
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 16]
Ripple resonance
Origin of synchrotron radiation in TCV
T. A. Wijkamp et al. Resonant interaction between runaway electrons and the toroidal magnetic field ripple in TCV. Nuclear Fusion, 64 (1):016021, 2023. DOI: 10.1088/1741-4326/ad0dd7.

## Slide 25: Analysis of the synchrotron radiation power
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 17a]

## Slide 26: Analysis of the synchrotron radiation power
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 17b]

## Slide 27: Analysis of the synchrotron radiation power
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 17c]

## Slide 28: Analysis of the synchrotron radiation power
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 18]

## Slide 29: Analysis of the synchrotron radiation power
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 19]

## Slide 30: Analysis of the synchrotron radiation power
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 20]

## Slide 31: Analysis of the synchrotron radiation power
 | 00 |  | 
 | 00 |  | 
 | 00 |  | 
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 21]
Notes: The RE densities (with the star) indicate the densities of the REs in the high-energetic vortex.

## Slide 32: Analysis of the synchrotron radiation power
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 22]
Notes: Higher loop voltage for #78817 (500 mV around <325 mV for the other shots.
Maybe the vortex can be replenished during the ECRH phase resulting in faster decay?

## Slide 33: Analysis of the synchrotron radiation power
 | 00 |  | 
 | 00 |  | 
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 23]

## Slide 34: Analysis of the synchrotron radiation power
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 24]
The loss coefficient, , becomes smaller if the ECRH power is deposited more radially outwards (except for #78817, possibly due to the higher loop voltage);
The high-energetic synchrotron radiation decay rate is higher than the lower-energetic PMTX decay rate.
The relative decrease of the (high-energetic) population of runaway electrons becomes smaller if the ECRH power is deposited more radially outwards;
If the ECRH power is deposited around the edge of the plasma, then the synchrotron radiation pattern does NOT completely disappear, indicating that some runaway electrons survive (within the core of the plasma);

## Slide 35: Analysis of the synchrotron radiation patterns
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 25a]

## Slide 36: Analysis of the synchrotron radiation patterns
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 25b - Hidden]

## Slide 37: Table of Contents
ECRH-induced expulsion of REs (model)
    Short recap of the zero-dimensional ECRH-induced expulsion of REs model;
    Analysis of the hard X-ray emission for different ECRH deposition locations;
Synchrotron radiation
    Introduction to the MANTIS system(s);
    Analysis of the synchrotron radiation power for different ECRH deposition locations;
    Introduction to the tomographic inversion tool(s);
    Analysis of the tomographic inversions of the RE-distribution(s);
Outlook
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 2]

## Slide 38: Tomographic inversion of the RE distribution(s)
SOFT: Synchrotron-detecting Orbit Following Toolkit
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 26]
M. Hoppe et al. SOFT: a synthetic synchrotron diagnostic for runaway electrons. Nuclear Fusion, 58 (2): 026032, 2018. DOI: 10.1088/1741-4326/aa9abb.
Notes: Guiding center distribution in terms of coordinates

## Slide 39: Tomographic inversion of the RE distribution(s)
SOFT: Synchrotron-detecting Orbit Following Toolkit
Input of SOFT:
    The angular distribution of the radiation power;
    The properties of the camera (aperture, distortion, position, spectral range, viewing angle and viewing direction, etc.);
    The magnetic field (strength) in the toroidal plane;
    The (runaway) electron distribution function;
Output of SOFT:
    The product of the Green function and the Jacobian (from first three inputs);
    The (absolute) intensity of the synchrotron radiation power (from all inputs);
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 27]
M. Hoppe et al. SOFT: a synthetic synchrotron diagnostic for runaway electrons. Nuclear Fusion, 58 (2): 026032, 2018. DOI: 10.1088/1741-4326/aa9abb.

## Slide 40: Tomographic inversion of the RE distribution(s)
Experimental results:
    The synchrotron radiation pattern(s) at different wavelengths from MANTIS II-b;
    The magnetic field (strength) in the toroidal plane;
Numerical results:
    The product of the Green function and the Jacobian;
‘Missing’ results:
    The (runaway) electron distribution function.
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 28]

## Slide 41: Tomographic inversion of the RE distribution(s)
SOLUTION: Tomographic inversion(s) of the synchrotron radiation pattern(s) from the different camera channels of MANTIS II-b.
Synchrotron radiation power recorded by the -th pixel:
Simultaneous Algebraic Reconstruction Technique (SART-algorithm):
    Minimizing difference between the synthetic image(s) and the camera image(s);
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 29a]
T. A. Wijkamp et al. Tomographic reconstruction of the runaway distribution function in TCV using multispectral synchrotron images. Nuclear Fusion, 61 (4): 046044, 2021. DOI: 10.1088/1741-4326/abe8af.
W. J. Roog. Synchrotron imaging as a diagnostic for runaway electron distribution on ASDEX Upgrade. Master Thesis, Eindhoven University of Technology, 2023.

## Slide 42: Tomographic inversion of the RE distribution(s)
Simultaneous Algebraic Reconstruction Technique (SART-algorithm):
    Minimizing difference between the synthetic image(s) and the camera image(s);
The SART-algorithm contribution
    Difference between synthetic and camera image weighted by Green function;
    Relaxation parameters governs the speed of convergence;
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 29b - Hidden]
T. A. Wijkamp et al. Tomographic reconstruction of the runaway distribution function in TCV using multispectral synchrotron images. Nuclear Fusion, 61 (4): 046044, 2021. DOI: 10.1088/1741-4326/abe8af.

## Slide 43: Tomographic inversion of the RE distribution(s)
Simultaneous Algebraic Reconstruction Technique (SART-algorithm):
    Minimizing difference between the synthetic image(s) and the camera image(s).
The penalty function contributions
    Provide smoothness on the solution in phase-space by providing penalties;
    Separate terms for the momentum-space grid, i.e. -grid, and the radial grid;
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 29c - Hidden]
T. A. Wijkamp et al. Tomographic reconstruction of the runaway distribution function in TCV using multispectral synchrotron images. Nuclear Fusion, 61 (4): 046044, 2021. DOI: 10.1088/1741-4326/abe8af.

## Slide 44: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 30a]

## Slide 45: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 30b]

## Slide 46: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 30c]

## Slide 47: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 31a]

## Slide 48: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 31b]

## Slide 49: Tomographic inversion of the RE distribution(s) Flat profile
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 32a]
1

## Slide 50: Tomographic inversion of the RE distribution(s) Edge-peaked profile
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 32b]

## Slide 51: Tomographic inversion of the RE distribution(s) Core-peaked profile
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 32c]

## Slide 52: Tomographic inversion of the RE distribution(s) Core-peaked profile
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 32d - Hidden]

## Slide 53: Tomographic inversion of the RE distribution(s)
Slightly edge-peaked profile shows best match with experimentally observed synchrotron radiation patterns.
Attempts have been made to fit radial profile. However, the shape of the resulting shape of the profile and the strong edge peaking in these radial profiles cannot be explained yet…
    More research (over the week) needed to come up with either …
      (i) a better fit (routine) of the radial profile;
      (ii) or an explanation of the resulting profile.
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 33]

## Slide 54: Tomographic inversion of the RE distribution(s) Core-peaked profile profile – Result of ‘‘ECRH’’
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 34]

## Slide 55: Outlook
Conclusion: ECRH-induced expulsion of REs is most efficient near-axis.
    (Effective) loss coefficient much larger near-axis compared to off-axis.
    Reduction of population of REs much larger near-axis compared to off-axis.
    In the off-axis shots, the synchrotron radiation does not completely disappear, and appears much brighter after the ECRH phase.
  Future work: Investigate the (shape of the) radial profile more thoroughly.
  Future-future work: Complete fluid-kinetic(-transport) DREAM simulations to numerically find the RE distribution.
      Fluid-transport DREAM simulations with frozen current mode already performed to get some insights in evolution of transport coefficient(s). More work needed to do…
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 35]

## Slide 56: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 36a - Hidden]

## Slide 57: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 36b - Hidden]

## Slide 58: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 36c - Hidden]

## Slide 59: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 36d - Hidden]

## Slide 60: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 37a - Hidden]
Notes: FIRST ATTEMPTS, NOT PRESENTED DURING REM, MORE RESEARCH NEEDED TO EXPLAIN (EVOLUTION OF) PROFILE

## Slide 61: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 37b - Hidden]
Notes: FIRST ATTEMPTS, NOT PRESENTED DURING REM, MORE RESEARCH NEEDED TO EXPLAIN (EVOLUTION OF) PROFILE

## Slide 62: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 37c - Hidden]
No specific changes in the radial RE distribution in the ‘middle’ of the (local) momentum-space distribution.
Decrease of near-axis peaks in the RE distribution(s) at the ‘top’ of the (local) momentum-space distribution. No significant changes in the off-axis peaks…
The (off-axis) ECRH-induced expulsion of REs seems to ‘bother’ only the on-axis population, while keeping the off-axis population intact, which results in much more synchrotron radiation after the ECRH phase.
Notes: FIRST ATTEMPTS, NOT PRESENTED DURING REM, MORE RESEARCH NEEDED TO EXPLAIN (EVOLUTION OF) PROFILE

## Slide 63: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 38a - Hidden]
Notes: FIRST ATTEMPTS, NOT PRESENTED DURING REM, MORE RESEARCH NEEDED TO EXPLAIN (EVOLUTION OF) PROFILE

## Slide 64: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 38b - Hidden]
Notes: FIRST ATTEMPTS, NOT PRESENTED DURING REM, MORE RESEARCH NEEDED TO EXPLAIN (EVOLUTION OF) PROFILE

## Slide 65: Tomographic inversion of the RE distribution(s)
Assessment of the runaway electron transport in ECRH-induced expulsion experiments
[Slide 38c - Hidden]
Notes: FIRST ATTEMPTS, NOT PRESENTED DURING REM, MORE RESEARCH NEEDED TO EXPLAIN (EVOLUTION OF) PROFILE