## Slide 1: Status of Collisionless Runaway Electron Mitigation Experiments
By:
A.F. Battey, H. Choudhury, P. Aleynikov, U. Sheikh, J. Decker, X. Tang, Q. Zhang, Y. Zhang, C. Paz-Soldan, D. Spong, Y. Ghai, W. Heidbrink, E. Hollman, C. Marini, A. Lvovskiy, S. Tang, C. Lasnier, B. Van Compernolle, J. Barr, D. Shiraki, N. W. Eidietis, M. Pandya, the DIII-D Team, LAPD, and MST teams
Affiliations:
Columbia University, Max Planck Institute for Plasma Physics, Swiss Federal Institute of Technology in Lausanne, Los Alamos National Lab, Oak Ridge National Lab, University of California Irvine, University of California San Diego, General Atomics, Lawrence Livermore National Lab, and University of Wisconsin-Madison
Presented to:
11th Runaway Electron Modeling Meeting
06/11/2024

## Slide 2: Motivation
Runaway electrons (REs) can be created during plasma start-up and tokamak disruptions
  Pose a severe risk to plasma-facing and water-cooled components
While the injection of high-Z impurities is capable of collisionally lowering the energy of REs it does not appear to be sufficient in machines with larger stored energy
  New mitigation techniques are therefore required
The low-Z benign termination technique has been shown to safely terminate dangerous RE beams on DIII-D and JET
The interaction with plasma waves has been shown to significantly alter the distribution function of relativistic electrons
Notes: I will begin with some quick motivations for the the implementation of a fully 3D electromagnetic code

## Slide 3: Outline
Low Density Runaway Electron Flushing
EC OXB Mode-Conversion Experiment
Benign Termination Experiment
Frontier Science Experiments
  LAPD
  MST
Conclusions

## Slide 4: Outline
Low Density Runaway Electron Flushing
EC OXB Mode-Conversion Experiment
Benign Termination Experiment
Frontier Science Experiments
  LAPD
  MST
Conclusions

## Slide 5: Relativistic Electrons Created in Multiple Regimes in DIII-D Device
QRE Regime: Created by lowering density and therefore
  Density lowered
  Loop voltage from solenoid begins to pull electrons into relativistic population
  Radiation from REs (ECE) detected by dud detection system
  Secondary gas puffed to raise density and cease RE production
  Experiment Conducted
In this regime REs carry a small percentage of the total plasma current
  Enables used of Gamma Ray Imager (GRI) Diagnostic
This regime is most similar to start-up runaway electrons vs. post-disruption beams

## Slide 6: X-Mode ECH Results in Flushing of Trace RE Population
Hari Choudhury
Observation made when X-mode ECH was applied to QRE plasmas:
  Hard X-ray quickly spikes
  Signal then slowly decays
The initial spikes occurs faster than the change in the background plasma parameters
  Believed to be immediate loss of particles to vessel wall
The slow decay is believe to be a result of the runaway electrons being ‘flushed’ from the plasma
  This assumption has been confirmed with recently obtained Gamma Ray Imager (GRI) data

## Slide 7: Combination of TCV and DIII-D Experiments Planned to Characterize Effect
To understand mechanism of flushing three effects need to be understood:
  Loop voltage (source)
  Density (sink)
  RE transport (sink)
Series of experiments completed on TCV to explore this effect studying effect of:
  EC power
  Injection location
TCV results: https://arxiv.org/pdf/2404.09900
DIII-D experiment attempts to measure this transport and determine the mechanism behind this effect
  Diagnostics: Beam Emission Spectroscopy and Radial Interferometer-Polarimeter
Hari Choudhury

## Slide 8: DIII-D Low Density Flushing Experiments Confirm TCV Power Scan Result
Up to 3MW of X-mode ECH applied to QRE plasmas in latest DIII-D experiments
  Power deposited on-axis
Decay of HXR faster with increased EC power
  Agrees with similar power scan completed on TCV
Similar to loop voltages measured for both 1MW and 3MW cases
  Hinting that a change in the RE source is not responsible for differences in flushing rate
Density comparable between different power cases
  Indicating that primary difference between cases is RE transport
Hari Choudhury

## Slide 9: Increase in ECH Power Observed to Alter Low Frequency Density Fluctuations
ECH power observed to drive broadband low frequency (<200kHz) density fluctuations for all flushing cases
Increase in EC power results in an increase in both power and frequency range of fluctuations
0-200kHz
t=6-9s
t=6-9s
t=6-9s
0.5 MW
1.1 MW
3.0 MW
Hari Choudhury

## Slide 10: Flushing Rate Observed to Correlate with Power of Fluctuations
Radial Interferometer Polarimeter (RIP) density fluctuations integrated from 10-200kHz to assess power of fluctuations
While the frequency range of fluctuations increases between 0.5 and 1.1 MW the power and RE flushing rate are comparable
The fluctuation power is observed to be the best indicator of HXR decay
  Comparable loop voltage and density indicates that the RE transport is most important
Hari Choudhury

## Slide 11: EC Current-Drive Results in Lower Flushing Rate than Pure Heating
Several shots were taken to explore the effect of heating vs. current drive on RE flushing
A significant difference in the flushing rate is observed for the heating vs. co-current drive cases
  Unable to get a counter-current case
Current hypothesis is that the current-drive results in an increase in RE production
  Loop voltage is the same
  Density is the same
  Fluctuation power is the same
Heating
ECCD
Hari Choudhury

## Slide 12: Outline
Low Density Runaway Electron Flushing
EC OXB Mode-Conversion Experiment
Benign Termination Experiment
Frontier Science Experiments
  LAPD
  MST
Conclusions

## Slide 13: Direct Wave-Particle Interaction Possible with Mode Conversion to Slow-X Mode
O and X-mode ECH polarization routinely used on DIII-D for heating and current-drive
Problem: These waves are incapable of interacting directly with runaway electrons
  Their parallel phase velocity is much greater than the speed of light
Solution: Mode conversion to slow-X (Z-mode)
  Launch O-mode wave
Requirements:
  Optimal parallel wave number, , or angle to magnetic field
  O-mode density cutoff within the plasma
X
O
sX
X
O
sX
Typical
Optimal
P. Aleynikov
Notes: As mentioned in the motivation slide we seek to identify an externally launched wave which is capable of modifying the runaway population. An obvious place to begin this search is the electron cyclotron wave.
Both O and X-mode polarizations of EC heating are routinely applied on DIII-D for both heating and current drive. However, we have a problem being that these two waves are incapable of interacting directly with the relativistic population since they both have a parallel phase velocity which is much greater than the speed of light.
The solution lies in a third branch of this wave which is shown the the dispersion relationships shown on the right side of this slide. On the top we the situation representative of a typical launching configuration where there is a distinct branch between the O-mode and the slow-X or Z-mode branch. However, there excists an optimal launching angle and therefore parallel index of refraction where the O-mode can smoothly transition to the slow-X branch.

## Slide 14: First OXB Mode Conversion Experiment Completed During Previous DIII-D Campaign
Two half day experiments allocated as part of the Frontier Science Program
First half day experiment measured successful OXB mode conversion
  Indicated by a peak in density near the edge of plasma
Increase in synchrotron power observed following OXB conversion
  Kinetic modeling indicates that this could be explain by increase in plasma density and/or wave-particle effects
Presence of helium used to raise plasma density resulted in 3D density structure
  Ionization near EC port
  Significantly complicates analysis
EC Begins at 600ms

## Slide 15: Second Half Day Designed to Answer Remaining RE Interaction Questions
Second half day experiment currently scheduled for June 14th!
  Flying back early from REM run experiment as session leader
Several steps will be taken to isolate the RE wave-particles effects:
  Pure D2 MGI will be used instead of helium to increase plasma density to O2 cutoff
  Delay will be taken between MGI and OXB application to allow Ar to be purged
New gyrotrons will allow direct comparison between X-mode, OXB, and non-OXB O-mode
P. Aleynikov

## Slide 16: Outline
Low Density Runaway Electron Flushing
EC OXB Mode-Conversion Experiment
Benign Termination Experiment
Frontier Science Experiments
  LAPD
  MST
Conclusions

## Slide 17: Background: Benign Termination Strategy
Technique being developed to safely terminate an existing RE beam
  Greatly increase energy deposition wetted area
  Does not rely in collisional damping
Procedure:
  RE beam is formed (killer Ar pellet)
  Secondary low-Z gas is puffed in (MGI) to recombined the background plasma
  Plasma equilibrium to driven towards low edge-q condition
    Increase plasma current
    Compress equilibrium (CP or VDE)
  Large MHD event terminates the plasma

## Slide 18: DIII-D Benign Termination Designed to Answer Remaining Benign Termination Physics
Experiment will be split into two back-to-back half days:
  MGI and fueling values will be used to scan the neutral pressure to identify recombination threshold
    Effect of RE-current
    Effect of Ar quantity
  Access to benign termination at high neutral pressures
    Effect of plasma current
    Effect of compression rate
Neutral partial pressure of D2 and Ar will be measured using Penning Gauges
Neutral pressure measurements will be compared to values obtained on European machines

## Slide 19: Outline
Low Density Runaway Electron Flushing
EC OXB Mode-Conversion Experiment
Benign Termination Experiment
Frontier Science Experiments
  LAPD
  MST
Conclusions

## Slide 20: Effect of Externally Injected Whistlers to be Studied on LAPD
Relativistic electrons will be created using the RF hot-electron ring source
  Maximum RE energy: 100s keV
  REs will have mainly perpendicular energy
Magnetic mirror configuration will be used with whistler waves fired along magnetic field line
Rough experimental plan:
  Create optimal pulse with low magnetic field (400G) and high density (4e12 cm-3).
  Helicon and scintillator diagnostic commissioning
  Scattering parameter scans (density and field)
H. Choudhury

## Slide 21: Plasma Parameters will be Leveraged to Explore Different Resonance Conditions
Colleagues at Los Alamos provided us with a momentum space engineering tool to explore resonance locations
  Numerical simulation employs the quasilinear diffusion operator in the relativistic Fokker-Planck equation
Predicts location of three primary Whistler resonances ()
  Inputs: Wave frequency, plasma density, toroidal field, electric field, theta, and Zeff
Location of resonance in momentum space depends on background plasma density and magnetic field
Co and Counter-injection allows different resonances to be selected
  Normal, Cherenkov, or Anomalous
H. Choudhury

## Slide 22: Outline
Low Density Runaway Electron Flushing
EC OXB Mode-Conversion Experiment
Benign Termination Experiment
Frontier Science Experiments
  LAPD
  MST
Conclusions

## Slide 23: Simulations Predict RE-Driven Slow-X Mode Decays to Whistler Modes
Kinetic+PIC simulation indicate that under conditions REs are capable of driving slow-X EC waves
  Can then parametrically decay to lower frequency whistler waves
Do to the high frequency and internal nature of these waves it is impossible to measure them on machines like DIII-D
Qile Zhang
s

## Slide 24: Experiments Designed to Explore Self-Excited Slow-X Wave on MST
Insertable fast magnetic probe on MST allows measurement of modes with
  Measures up to 6GHz (
  Can be inserted directly into the edge of the plasma
Work will follow-up on previously completed runaway electron experiments
Experiments will be broken into two phases:
  Develop new high energy runaway target plasma
    Expected to need >1MeV
  Attempt to measure the slow-X mode and possible children modes
    Children modes will be determined using observed wave parameters
Results will then be compared to modeling completed by Los Alamos colleagues
  Xianzhu Tang and Qile Zhang
MagNetUS Website
MST Team

## Slide 25: Outline
Low Density Runaway Electron Flushing
EC OXB Mode-Conversion Experiment
Benign Termination Experiment
Frontier Science Experiments
  LAPD
  MST
Conclusions

## Slide 26: Conclusions
Recently completed experiments show correlation between power of low frequency fluctuations and RE flushing rate
Second half day experiment will explore effect of slow-X mode on REs
  Will attempt to obtained O2 cutoff density with minimal impurities
Benign termination experiment later this year will explore the physics of recombination and technique at elevated neutral pressure
The effect of externally launched whistler waves will be studied will be studied using the helicon antenna on LAPD
High frequency insertable probe on MST allows for the direct measurement of self-excited slow-X mode and ‘child’ whistler modes