## Slide 1: Runaway Electron Generation during Tokamak Disruptions
Chris McDevitt
University of Florida
Thanks to Xianzhu Tang, Nathan Garland
Work supported by TDS & SCREAM SciDACs

## Slide 2
Tokamak Disruptions Present a Diverse Range of Physics and Modeling Challenges
Large scale 3D dynamics
  B fields  stochastic
Transport takes on 3D features
  Parallel transport dominates
Compared to a confined plasma, entirely new set of physics issues arise
  Radiation by copious amount of high-Z impurities
  Relativistic runaway electrons

## Slide 3: Motivation
Focus here is on the self-consistent description of runaway electron dynamics during a tokamak disruption
Initial focus is on axisymmetric geometry
  Provides testbed for fluid-RE coupling schemes
  Seek to develop a drift-kinetic based runaway electron solver incorporating essential runaway electron physics
Use of drift-kinetics allows first principle treatment of a range of physical processes of relevance to runaway dynamics

## Slide 4: Outline
Some challenges of runaway electron modelling in axisymmetric geometry
  Runaway seed formation
  Avalanche amplification
  Impact of runaway electrons on background impurities
Self-consistent runaway formation in an axisymmetric plasma
  Hot tail formation
  Runaway formation during the current quench

## Slide 5: Drift Kinetic Description of Runaway Electrons
Particle based drift-kinetic solver for 3D-2V runaway electron population employed throughout this presentation [McDevitt et al. 2019]
Relativistic guiding center evolved via:
Large-angle collisions described by a Möller source
Small-angle collisions treated by Monte Carlo collision operator
  Partial screening included [Hesslow et al. 2017]
Synchrotron radiation damping incorporated

## Slide 6: Why Drift-Kinetics?
Runaway electron dynamics can be described most efficiently employing reduced slab or bounce-averaged formations
  Both approaches remove the rapid transit motion of an electron along a magnetic field line
Drift-kinetic descriptions are often employed to capture the loss of RE’s along open field lines [Izzo et al. 2011, Sommariva et al. 2018, del-Castillo-Negrete et al. 2018]
Here we seek to show that even in axisymmetric geometries, drift kinetic formulations can differ significantly from the slab or bounce formulations
  Provide useful reference point for verifying reduced simulations

## Slide 7: Runaway Generation Processes in Tokamak Plasmas for Large Inductive Electric Fields
Our intuition of how toroidal geometry impacts runaway generation is largely based on electron trapping
  Implies a reduction of runaway generation as the minor radius is increased [Rosenbluth-Putvinski 1997]
The critical energy for an electron to run away in a hydrogen plasma can be approximated by:
For large electric fields this energy can be several hundred eV
  Electrons at these modest energies are often characterized by
Collisionality at Critical Energy
Critical Energy

## Slide 8: Runaway Probability Function in Toroidal Geometry: Weak Inductive Electric Field
Interesting to contrast the runaway probability function (RPF) [Liu et al. 2016, Zhang et al. 2017] for r/a=0 and r/a=0.8
  Radiation neglected here → electrons accelerated to arbitrarily high energy are deemed runaways
  Electrons that reach the thermal energy are deemed to not run away
The RPF exhibits a strong local minimum at for the off-axis case
  Significantly reduces the efficiency of runaway generation at large minor radius
r/a=0 for E/Ec=10
Trapped
region
r/a=0.8 for E/Ec=10

## Slide 9: Runaway Probability Function in Toroidal Geometry: Strong Inductive Electric Field
For strong inductive electric fields, off-axis RPF no longer strongly reduced in “trapped” region
  The large collisionality near the critical energy to run away prevents electrons from completing a bounce orbit
  Impact of electron trapping is largely negated
r/a=0 for E/Ec=1000
r/a=0.8 for E/Ec=1000

## Slide 10: Inductive Electric Field During a Tokamak Disruption
The characteristic strength of the inductive electric field can be estimated based on the available poloidal flux [Boozer 2018]
An ITER-like case with of poloidal flux and a current decay implies an average loop voltage of
  This implies for ne=1014 cm-3, Te=10 eV, and
Maximum inductive electric field generally much larger
JET-like case
[Smith et al. 2006]

## Slide 11: Runaway Electron Generation is Strongly Localized for Large Electric Fields
For a large inductive electric field electrons can gain a significant amount of energy in a single toroidal transit
Specifically, for an ITER-like case with an average loop voltage of
  An electron can gain up to during a single toroidal transit
  The critical energy at this electric field is
  Electrons can more than double their energy in a single toroidal transit
  For , electrons can be accelerated before sampling the entire flux surface
The inductive electric field in tokamak geometry scales as
  Implies strong poloidal localization of runaway generation for large inductive electric fields

## Slide 12: Runaway Probability Function in Configuration Space
In the low collisionality limit and a modest inductive electric field
For large inductive electric fields the RPF is no longer a flux surface function 
  The strong in-out asymmetry results from
  A weaker up-down asymmetry results from helicity of magnetic field line
RPF substantially increased across poloidal cross section for large inductive electric field
  Significant increase in efficiency of all runaway generation processes
E/Ec=10
E/Ec=1000

## Slide 13: Outline
Some challenges of runaway electron modelling in axisymmetric geometry
  Runaway seed formation
  Avalanche amplification
  Impact of runaway electrons on background impurities
Self-consistent runaway formation in an axisymmetric plasma
  Hot tail formation
  Runaway formation during the current quench

## Slide 14: Seed Runaway Formation: Dreicer Production in Tokamak Geometry
Considering Dreicer production as a function of electric field strength
  held constant while the temperature is scanned
  Noting  results in the strength of electric field being varied
For modest values of the inductive electric field (high temperature) the results from Nilsson et al. 2015 are reproduced
For large inductive electric fields (low temperature) the present results deviate qualitatively from previous predictions
  Dreicer production more efficient at larger minor radii
Radial Variation of Dreicer Production

## Slide 15: Runaway Distribution near Threshold Energy Strongly Asymmetric
Noting the modulation of inductive electric field
  Runaway electrons more efficiently accelerated on inboard side
  Less efficiently on outboard side
Poloidal modulation does not cancel:
  Dreicer production depends non-linearly on the electric field strength
Critical energy
to run away
Poloidal dist.
of electrons
at critical energy
E/Ec=3000, Te=10 eV
E/Ec=300, Te=100 eV

## Slide 16: Avalanche Amplification for Large Electric Fields
Related physics impacts avalanche amplification
High collisionality at critical energy negates “neoclassical” reduction factor
However, the avalanche growth rate is (approximately) linear with respect to the electric field:
  modulation of inductive electric field will (nearly) cancel
  Little to no increase expected at large minor radii for asymptotically large electric fields
Hydrogen plasma

## Slide 17: Outline
Some challenges of runaway electron modelling in axisymmetric geometry
  Runaway seed formation
  Avalanche amplification
  Impact of runaway electrons on background impurities
Self-consistent runaway formation in an axisymmetric plasma
  Hot tail formation
  Runaway formation during the current quench

## Slide 18: Collisional-Radiative Modeling with Runaways
FLYCHKLite allows relativistic corrections & arbitrary electron distribution
QED effects manifest at relativistic e- energies
Enhanced coupling increases cross-section, so called Breit interaction
Conventional cross-section
nAr = 1014 cm-3 ; Runaways carry an ITER-like current (~10 MA)
Predicts very different charge state distribution & radiation power loss
Garland et al. 2019

## Slide 19: Charge state distribution of cooling Ar with 5 MeV Gaussian tail
Charge state distribution spread as plasma cools is crucial to e- scattering
Runaway tail yields greater number of ions to scatter from and with higher charge
Garland et al. 2019

## Slide 20: Outline
Some challenges of runaway electron modelling in axisymmetric geometry
  Runaway seed formation
  Avalanche amplification
  Impact of runaway electrons on background impurities
Self-consistent runaway formation in an axisymmetric plasma
  Hot tail formation
  Runaway formation during the current quench

## Slide 21: Runaway Electron Formation: Axisymmetric Plasma
Interested in utilizing the above drift-kinetic solver for describing RE generation/evolution across a range of plasma conditions
The current focus is on the axisymmetric limit with circular flux surfaces
  Future work will consider a self-consistently evolving 2D magnetic equilibrium
The present approach allows for:
  The evaluation of RE formation for general a collisionality regime
  Provides testbed for fluid-RE coupling schemes

## Slide 22: Coupling RE’s to Inductive Electric Field
Will evolve the induction equation
Along with a modified Ohm’s law [Rosenbluth-Putvinski 1997]:
evaluated from kinetic solution
Density and temperature profiles taken as inputs at present
  fully ionized hydrogen plasma assumed
  Future work will incorporate self-consistent atomic physics model
Assumed Te evolution

## Slide 23: Capturing Seed Runaway Electron Mechanisms
Incorporating seed mechanisms requires resolving both the tail and bulk plasma non-perturbatively
  Only a tiny fraction of electrons run away
  Presents significant challenge for particle based approaches
Variable weight scheme employed to improve resolution of tail population: marker particles split as they are accelerated
  Only tail electrons fed back into field solve

## Slide 24: Example of Runaway Electron Formation
Runaway generation occurs in three distinct phases
Hot tail generation:
  Strongly non-Maxwellian solution due to rapid thermal quench
Avalanche amplification:
  Seed population amplified until RE’s overtake plasma current
JET like shot with a thermal quench of 𝜏TQ=0.5 ms assumed in this example

## Slide 25: Example of Runaway Electron Formation (cont’d)
A significant fraction of the initial current is converted into runaway electron current
  The converted fraction depends sensitively on thermal quench time
Resulting runaway current profile is strongly peaked
  Leads to a reduction of the on-axis safety factor
Itot
IRA
Itot-IRA

## Slide 26: Summary
Runaway probability function found to have a non-trivial structure in the 4-D phase space
  Runaway distribution function is not well approximated as a flux surface function near critical energy to run away
The efficiency of runaway generation processes found to be strongly modified in the limit of large inductive electric fields
  Dreicer production rate is found to be enhanced at finite minor radii
  Avalanche amplification found to be approximately constant in radius
Runaway generation coupled to a self-consistently evolved electric field in tokamak geometry
  Provides high physics fidelity description of 2D-2V runaway electron phase space evolution

## Slide 28: Parallel Electric Field in Axisymmetric Tokamak Geometry
Incompressibility , but implies [Helander-Sigmar]
For a low-beta poloidal plasma, ⇐ Flux surface function
From Ohm’s law
In simplest limit ,
More complex cases possible for poloidally and toroidally localized impurity deposition  treat in future work

## Slide 29: Impact of Impurities on Runaway Probability Function
Presence of impurities modifies the collisionality via two partially compensating trends
Critical energy to runaway increased
Pitch-angle scattering more efficient at a given energy
r/a=0.8, E/Ec=300, Zeff=1
r/a=0.8, E/Ec=300, Zeff=5
Weak field side
Weak field side

## Slide 30: Impact of Impurities on Avalanche Amplification
Presence of impurities only modestly impact radial modulation of avalanche amplification factor
  Amplification factor reduced as radius is increased for small
  Amplification factor approximately constant for large

## Slide 31: Impact of Impurities on Runaway Probability Function: Partially Ionized Plasma
Presence of partially ionized impurities modifies the collisionality drastically increases critical energy to runaway
  Pitch-angle scattering also drastically increased at a given energy
r/a=0.8, E/Ec=300,
r/a=0.8, E/Ec=300,
Hesslow et al. 2017
Weak field side
Weak field side

## Slide 32: Impact of Impurities on Avalanche Amplification : Partially Ionized Plasma
Presence of partially ionized impurities only modestly impact radial modulation of avalanche amplification factor
  Amplification factor reduced as radius is increased for small
  Amplification factor approximately constant for large