## Slide 1: MHD simulations of runaway electron avalanche in ITER mitigated disruptions
Chizhou WANG
Jonathan GRAVES
Mengdi KONG
Javier ARTOLA
Eric NARDON

## Slide 2
Runaway electron deconfinement in current quench
MHD stability during the current quench under different current profiles
Evaluation of runaway electron risk in two current quench simulations
Conclusions and outlook

## Slide 3: MHD instability in disruptions
[1] F.J. Artola, et al. NF 2022.
[2] L. Carbajal, et al. PP 2020.
During RE avalanche…
  Some flux surfaces (FS) have recovered after thermal quench (TQ).
  MHD instabilities (tearing/kink modes) might grow again in cold (~10 eV) plasma [1].
  Overlapping modes lead to magnetic stochasticity. RE loss rate increases in stochastic field.
  If RE avalanche is terminated by strong loss when IRE is still small, damage from a large RE beam can be prevented.[2]
[Growth rate goes up with resistivity]

## Slide 4: MHD instability in disruptions
Topic of this project: could the RE loss from MHD instabilities prevent the formation of a large IRE(>150kA) in ITER disruptions from Ip=15 MA?
Problems:
  Post-TQ plasma scenario is unknown.
  3D simulation of entire CQ (~100ms) is expensive.
We investigate 2 scenarios:
  Worst-case scenario where MHD activities are relatively mild. High RE risk.
    MHD modes’ stability is decided by global j profile, while their growth rates are related to local j gradient.
    Scan over j profile on simplified JOREK simulations for stable cases.
  A relatively realistic post-TQ plasma scenario.

## Slide 5: Growth of instabilities
Flat core j profile
j~0 outside LCFS
Steep j gradient on edge
Strong current drive on
edge rational surfaces
1) 5/2 and 3/1 modes driven on edge
n=1 plot, t=0.84ms
n=2 plot, t=1.18ms
Edge modes widen, perturbate inner rational surfaces
2) 2/1 triggered by growing 3/1
n=1 plot, t=7.12ms
3/1 mode grows and widens
From Wesson [3]
[3] J. Wesson, D. J. Campbell. Tokamaks.

## Slide 6: More detailed CQ simulations using 2 j profile examples
2 initial j profiles (more realistic than Wesson’s) based on previous scan:
  Case 1: peaked, like, used as worst-case scenario
  Case 2: flat, used as a more realistic reference
Simulation setup on JOREK code:
  5 toroidal harmonics n=1-5, initial mode energies ~10-10En=0 (<~ post-TQ reality)
  Free-boundary conditions via JOREK-STARWALL coupling
  Impurity radiation (Prad) and Ohmic heating (Pohm) added; Temperature from self-evolution
  ne=3.9*1020 m-3, nNeon= 6.1*1018 m-3, homogeneous.
RE fluid model:
  Artificial Iseed = 10 mA at t=0
  The only source: avalanche

## Slide 7: RE fluid parallel transport
Most realistic: advection, , typical loss time (L: connection length to the wall)
  Very small (increase with stochasticity, eventually <0.005 jorek unit (JU)) is required. Unfeasible.
Simplified model: parallel diffusion, , typical loss time
  To simulation realistic RE loss with parallel diffusion,
    ~ in open field lines (L~0.1 m)
    in stochastic field (L~100 - 10000 m), required.
  Compromise: instead of , ensure that RE is lost fast enough
    Realistic RE-MHD interaction: ; unnecessary if
    Similar jRE evolution to advection: on open or stochastic field lines - in stochasticity (), still a heavy computation load for ~10 ms simulations

## Slide 8: RE fluid parallel transport
First stage simulations: = to study RE population semi-quantitatively
  is valid when IRE<150 kA. REs’ feedback to MHD is negligible.
  nRE in stochastic region may be over-estimated (under-estimated loss).
  nRE in closed FSs (loss is negligible) could be well estimated.
Realistic RE transport in stochastic field is investigated by tracing particles ()
Potential results:
  IRE<150kA when field lines become completely stochastic. All REs are lost under a safe IRE.
  IRE reaches MA level with most of it in closed FSs (L). High RE risk exists.
  Intermediate case: more precise RE transport model is needed.

## Slide 9: More detailed CQ simulations: Case 1
particle tracing: 10 MeV REs, 0.99 pitch
Emag grows slowly after 1/1 kink mode decays. Core region is well confined after 48 ms.
IRE~100kA, Ip = 10 MA by t=49 ms.
Underestimated stochasticity transport is not a problem with most REs in confined region.
IRE is expected to saturate in another 10 ms if core FSs stay closed.
t=48.5ms
t=48.5ms

## Slide 10: Push case 1 further?
More FSs collapse due to 2/1 mode
Boosted by slow RE transport?
Core FSs and 2/1 island recover
Due to ~1 MA IRE?
RE-MHD interaction is unrealistic at this stage (jRE~>johm in the core) and beyond the goal of current project.

## Slide 11: More detailed CQ simulations : Case 2
particle tracing: 10 MeV REs, 0.99 pitch
Fast mode growth. Global stochasticity after 5.3 ms.
L<104 m. All REs should be lost within 0.03 ms when IRE is still negligible.
RE loss rate underestimated in fluid model using =.
t=5.3ms
t=5.3ms

## Slide 12: Conclusions
No linearly stable j profiles have been found so far in post-TQ ITER plasma: edge modes always grow.
Peaked j profiles are more stable, where REs have time to avalanche.
Under flat-plateau j profile (what we may expect in reality), magnetic lines get stochastic rapidly and REs are thus deconfined. RE avoidance on ITER could be more promising than expected.
Problems
Only a qualitative estimation of RE risk under different post-TQ current profiles is made. What happens under IRE~>102 kA is not available without a refined transport model.
Since the temperature plays an important role in the mode growth rates and is determined by Pohm and Prad, homogeneous impurity density may not be proper.

## Slide 13: Outlook: more realistic RE avalanche and transport
ITER disruption simulations:
  More realistic plasma scenario: mode energies, profiles of current, density, impurity, and temperature from TQ simulations will be used [4].
  RE transport:
    After magnetic stochasticity grows to the high nRE region (core plasma), DRE,// will be increased to >109 m2/s to mimic fast RE transport.
    Stay on particle tracing if it is enough to evaluate the RE risk or 1) is proven to be too expensive.
Cooperation with BEST team:
  First-principle RE modeling for BEST tokamak (EUROfusion & IPP-CN).
[4] D. Hu, et al. NF 2021.

## Slide 14: Runaway electrons in tokamak disruptions
Runaway electrons (RE):
Very high energy electrons generated in tokamaks
[1]
    During disruptions:
[1] A. Boozer. PoP, 22(3), 03 2015.
Current quench (CQ)
~102 ms
Fast electrons with low collision rates (seeds);
(1)
(2)
RE
Avalanche via close collisions with thermal electrons.
(3)
RE
RE
RE
High current remains in cold, resistive plasma:
Strong loop electric field ()
Ip
Thermal quench (TQ) ~1 ms
Confinement lost
Confinement (partially) recovered

## Slide 15: Runaway electrons in ITER disruptions
(2) IRE saturates. Majority of Ip carried by REs.
Majority of Ip carried by IOhm
Emag on IOhm
Emag on IRE
(1) Exponential growth of IRE
RE avalanche gain:
>1016 in ITER disruptions with Ip=15MA
(3) Termination on the wall.
Ek of REs
Ohmic heating
Radiation
IRE: the current carried by REs

## Slide 16: RE deconfinement in ITER current quench
If RE avalanche is terminated by strong loss when IRE is still small, damage from a large RE beam can be prevented.
REs are lost once magnetic flux surfaces (FS) are opened or destroyed.
[3] C. Wang, et al. NF 2025.
[4] V. Bandaru, et al. JPP 2025.
Icore
Ihalo
Plasma vertical motion
RE
RE
  FSs open due to vertical motion
    Plasma moves vertically in disruptions. REs are lost on opened field lines (halo region).
    IRE after avalanche can be greatly reduced [3,4], only ~kA in marginal cases.
    A bit more RE loss may make RE avoidance work on ITER…

## Slide 17: Scan over j profiles
MHD modes’ stability is decided by global j profile, while their growth rates are related to local j gradient.
Wesson’s current density profile with one parameter [3]:
Lower : flat j and q profiles; higher : peaked j and q profile
3D MHD simulation using JOREK (toroidal harmonics n=1,2,3)
  Fixed boundary
  Fixed temperature and density profiles
Plasma parameters (ITER-like, after hydrogen injection and TQ):
[3] J. Wesson, D. J. Campbell. Tokamaks.
Main species | B0 | ne,core | Te,core | Ip0
Hydrogen | 5.3 T | 5x1020 m-3 | 10 eV | ~15 MA (may change slightly under different profiles)

## Slide 18: Scan over j profiles
: high initial growth rate due to 1/1 kink mode. Stabilized after q=1 FS vanishes.
: saturates at high level; completely stochastic magnetic field.
: saturates at ~0.1 MJ, then decays to ~0.01 MJ. Closed FSs still exist.
Solid: n=1
Slashed: n=2
Dotted: n=3

## Slide 19: RE fluid diffusion model : transport before stochasticity
Corrected RE avalanche model; add Dhyper=1d-10 JU and tgnum_nre=2 to enable larger dt~0.1
Before stochasticity grows to core plasma, IRE is insensitive to transport model.
DRE,// = 106 m2/s is adequate for early stage of CQ to save computational resource.

## Slide 20: RE fluid diffusion model : transport in stochastic field
Scan over DRE,// within 0.04 ms under global stochasticity
  Observable RE loss start from DRE,// =1d9 m2/s with
  Advection model with is running for benchmark.
  dt = 0.02 for DRE,// =1d9 m2/s; dt < 0.01 for DRE,// =1d10 m2/s. Unfeasible for ~1 ms (3000 JU) simulation.

## Slide 21: Current profile evolution
Case 1
Case 2

## Slide 22: Outlook: more realistic RE avalanche and transport
On simulations:
  More realistic plasma scenario: mode energies, profiles of current, density, impurity, and temperature from TQ simulations will be used [8].
  After magnetic stochasticity grows to the high nRE region (core plasma), DRE,// will be increased to >109 m2/s to mimic RE transport in stochastic field lines.
  Hypothesis: post-TQ MHD is unstable like Case 2. Magnetic stochasticity grows from marginal to global within 1 ms. The corresponding high DRE,// phase with small dt (<0.1 JU) won’t last long. Core*hour consumption ~1M.
On code:
  Under small limit, nre evolution equations could be decoupled with MHD equations: MHD is solved without REs, then the RE fluid evolution is solved based on the resulting fields, like in the particle model. Different dt might be applied to MHD and RE fluid evolution to save CPU hours.
[8] D. Hu, et al. NF 2021.