## Slide 1: Design of the TCV Runaway Electron Mitigation Coil
A. Battey, U. Sheikh, F. Crisinel, J. Decker, D. Fasel and, Y. Liu
REM – 5th June 2025

## Slide 2
Introduction
Design
Resistance Scan
Scenario Scan
Position Scan
Conclusions and Future Work
OUTLINE

## Slide 3: Basics: Runaway Mitigation Coil
REMCs have the added advantage of being passively driven and therefore do not require disruption prediction
  Current in the coil is driven by the loop–voltage produced during the CQ
Runaway electron mitigation coil (REMC) is a promising tool for mitigating runaway electrons (REs)
  Prevents runaway electrons by deconfining the seed population
  Deconfines existing REs
REMCs have been designed for several tokamaks
  Installed: HBT-EP
  Planned: TCV, SPARC, and DIII-D
TCV
SPARC
DIII-D

## Slide 4: REMC Currently Under Development for the TCV Tokamak
The TCV REMC aims to be the first to operate in the presence of a runaway electron beam
  Installation planned for later this year
TCV REMC will have less constraints that future high-field or high plasma current tokamaks
  Less mechanical forces due to lower field
  Less current carried in coil

## Slide 5: REMC Currently Under Development for the TCV Tokamak
The small size and flexibility of TCV also allow for the possibility of testing multiple coil geometries
  1St: Max
  2nd: Maximize resonance with rational surfaces?
Coil will be designed to drive maximum n=1 field amplitude to allow for maximal radial extent
  Made of copper with a rectangular cross-section
  Behind the plasma-facing tiles on the HFS

## Slide 6: REMC Currently Under Development for the TCV Tokamak
Due to the lower Ip, the biggest challenge will be coupling to sufficient plasma current
  Limited space behind the plasma-facing tiles is a major constraint on the maximum cross-section of the coil
  The contact resistance of the coil elbows will need to be minimized
Looking into techniques to keep the coil resistivity as low as possible
  Possibly using polished gold/silver joints
  Expanding coil cross-section where possible
The coil will be insulated from the nearby wall/tiles with spray-on insulating coating
  Kapton or Al2O3
  Currently testing Kapton samples for outgassing

## Slide 7: Special Runaway Scenario Being Developed for TCV REMC
Typical RE scenario on TCV relies on low-density to produce seed runaway populations

## Slide 8: Special Runaway Scenario Being Developed for TCV REMC
Typical RE scenario on TCV relies on low-density to produce seed runaway populations
Step 1: Density is lowered by reducing fueling

## Slide 9: Special Runaway Scenario Being Developed for TCV REMC
Typical RE scenario on TCV relies on low-density to produce seed runaway populations
Step 1: Density is lowered by reducing fueling
Step 2: Low critical electric field allows for a seed RE population to grow

## Slide 10: Special Runaway Scenario Being Developed for TCV REMC
Typical RE scenario on TCV relies on low-density to produce seed runaway populations
Step 1: Density is lowered by reducing fueling
Step 2: Low critical electric field allows for a seed RE population to grow
Step 3: MGI triggers current quench
  Avalanche mechanism results in full conversion to RE current
MGI

## Slide 11: Special Runaway Scenario Being Developed for TCV REMC
A new scenario has recently been developed that induces a current quench in the presence of a RE beam
  NBI is used to trigger CQ

## Slide 12: Special Runaway Scenario Being Developed for TCV REMC
A new scenario has recently been developed that induces a current quench in the presence of a RE beam
  NBI is used to trigger CQ

## Slide 13: Special Runaway Scenario Being Developed for TCV REMC
A new scenario has recently been developed that induces a current quench in the presence of a RE beam
  NBI is used to trigger CQ
Scenario with partial current quench used for simulations
  This is very likely to improve in the future
Experimental time is also scheduled to develop a DIII-D/AUG type disruption scenario
  Where REs are produced primarily through hot-tail mechanism

## Slide 14: ThinCurr Model Models 3D Conducting Structures as a Series of Coupled Circuit Equations
Workflow begins with a CAD model of the tokamak conducting structures
These models are then defeatured to reduce computational time
  Important details such as portholes, stability plates, or structural elements are retained
These surfaces are then meshed to the desired resolution
  Different components can have higher/lower resolution
Different materials or thicknesses can all be captured in a single model
  TCV has 2 resistivities
  DIII-D model has 4 resistivities
TCV

## Slide 15: ThinCurr Model Models 3D Conducting Structures as a Series of Coupled Circuit Equations
Physics governed by inductance/resistance
Additional currents/voltages can be included
  Filament coils ( or )
  Plasma “modes” (eg. DCON)
Magnetic fields can be calculated anywhere in space or time
  Sensor signals with eddy currents
  Lorentz forces on structures
  Discontinuities in at surfaces

## Slide 16: REMC Geometries Evaluated Using ThinCurr and MARS Codes
Step 1: ThinCurr will be used to evaluate all possible coil shapes
  Enabled by its quick/inexpensive run-time
This step will allow use to select several leading coil candidates using performance metrics:
  Maximum induced coil current
    Coils with < 10% Ip will be eliminated
  Applied n=1 field at plasma surface
    DIII-D studies highlighted the benefits of both maximum amplitude and broadness of perturbation

## Slide 17: REMC Geometries Evaluated Using ThinCurr and MARS Codes
Step 2: The top three candidates will be modeled with the MHD code MARS-Q to determine their ability to drive beneficial MHD
  A workflow was developed to allow the 3D fields from ThinCurr to be passed into MARS
  Relativistic test particles will then be used to assess the effect of the coil

## Slide 18
Introduction
Design
Resistance Scan
Scenario Scan
Position Scan
Conclusions and Future Work
OUTLINE

## Slide 19: Mounting Location Limits Possible to Geometries
Horizontal channels exist behind the tiles at 12 vertical locations
Vertical coil legs can then be added between any of the 16 vessel sections
Assuming a symmetric coil, this allows for a total of 9 coil designs
Coils are parameterized based on their vertical height and number of horizontal segments
  x6 2-segment coils
  x2 4 segment coils
  x1 8-segment coils

## Slide 20: ThinCurr Studies Explore the Effect of Coil Resistivity on Coil Performance
Due to pre-disruption plasma current of TCV the success of the coil will rely keeping the resistivity as low as possible
  Difficult with the limited space behind tiles
  Installation limitations also prevent the coil from being one solid piece
    Therefore, low-resistance joints are essential
ThinCurr estimates the minimum possible coil resistivity of assuming a simple hoop at the HFS midplane
  Assume a cross-section of 4cm x 1cm behind tile

## Slide 21: Coil Resistivity Explored for All Possible Geometries
The resistivity of all possible coil geometries was explored (50-500 )
  Determined limits will then be shared with the engineering team

## Slide 22: Coil Resistivity Explored for All Possible Geometries
The resistivity of all possible coil geometries was explored (50-500 )
  Determined limits will then be shared with the engineering team
Example: 4-segment coil with vertical height 34.5cm
  Top candidate due to its ability to couple to the CQ and drive broad perturbation

## Slide 23: Coil Resistivity Explored for All Possible Geometries
The resistivity of all possible coil geometries was explored (50-500 )
  Determined limits will then be shared with the engineering team
Example: 4-segment coil with vertical height 34.5cm
  Top candidate due to its ability to couple to the CQ and drive broad perturbation
Resistivity affects both the maximum induced coil currents and the time response of the coil
10%
5%

## Slide 24: Coil Resistivity Explored for All Possible Geometries
Both the vertical and radial n=1 fields are then measured at the plasma surface

## Slide 25: Coil Resistivity Explored for All Possible Geometries
Both the vertical and radial n=1 fields are then measured at the plasma surface
Predictions on required to successfully mitigate REs vary in the literature

## Slide 26: Coil Resistivity Explored for All Possible Geometries
Both the vertical and radial n=1 fields are then measured at the plasma surface
Predictions on required to successfully mitigate REs vary in the literature
  Boozer:
    Boozer 2011 PPCF

## Slide 27: Coil Resistivity Explored for All Possible Geometries
Both the vertical and radial n=1 fields are then measured at the plasma surface
Predictions on required to successfully mitigate REs vary in the literature
  Boozer:
    Boozer 2011 PPCF
  Helander:
    Helander 2002 PPCF

## Slide 28: Coil Resistivity Explored for All Possible Geometries
Both the vertical and radial n=1 fields are then measured at the plasma surface
Predictions on required to successfully mitigate REs vary in the literature
  Boozer:
    Boozer 2011 PPCF
  Helander:
    Helander 2002 PPCF
Important: Due to the inductance of the coil and eddy currents the maximum field is often applied after the CQ
  The performance of the coil is evaluated using the field at

## Slide 29: Coil Resistivity Explored for All Possible Geometries
The performance of 5 possible coil geometries is compared using:
  Maximum REMC current
  Vertical field at 75% of TQ time
  Radial field at 75% of TQ time

## Slide 30: Several Coil Geometries Eliminated with Resistivity Scan
The performance of 5 possible coil geometries is compared using:
  Maximum REMC current
  Vertical field at 75% of TQ time
  Radial field at 75% of TQ time
2-legged coils:
  Getting close to midplane results
  in more current
  Comparable radial field
  Less vertical field than 4-legged
These coils will have the lowest resistivity of all possible coils
  11.5 cm coil will therefore couple to the most current

## Slide 31: Several Coil Geometries Eliminated with Resistivity Scan
The performance of 5 possible coil geometries is compared using:
  Maximum REMC current
  Vertical field at 75% of TQ time
  Radial field at 75% of TQ time
4-legged coil:
  In order to keep the coil
  symmetric height needs
  to be 1.035 m
    Making it the tallest coil
  This large height results in low coupling to the CQ
    Disqualified based on 0.05 * Ip evaluation parameter

## Slide 32: Several Coil Geometries Eliminated with Resistivity Scan
The performance of 5 possible coil geometries is compared using:
  Maximum REMC current
  Vertical field at 75% of TQ time
  Radial field at 75% of TQ time
8-legged coil:
  The average height of
  horizontal legs determined
  the induced current
    Therefore, this coil is able to couple to a significant current at comparable resistivity
  However, the resistivity of the coil increases with the number of joints
    This, along with increased complexity, disqualifies this coil

## Slide 33
Introduction
Design
Resistance Scan
Scenario Scan
Position Scan
Conclusions and Future Work
OUTLINE

## Slide 34: ThinCurr Leveraged to Explore the Effect of Potential RE Scenarios
TCV scenario is still being developed and is likely to improve
ThinCurr studies completed to explore how these potential improvements will affect coil performance
Two parameters explored:

## Slide 35: ThinCurr Leveraged to Explore the Effect of Potential RE Scenarios
TCV scenario is still being developed and is likely to improve
ThinCurr studies completed to explore how these potential improvements will affect coil performance
Two parameters explored:
  Change in plasma current during the current quench

## Slide 36: ThinCurr Leveraged to Explore the Effect of Potential RE Scenarios
TCV scenario is still being developed and is likely to improve
ThinCurr studies completed to explore how these potential improvements will affect coil performance
Two parameters explored:
  Change in plasma current during the current quench
  The current quench time,

## Slide 37: Current Quench Time Scan
Current quench is modeled as a linear ramp down of the current
  The current profile is shifted down rigidly
As expected, the shorter current quench times results in greater maximum current
However, due to multiple effects, there is an optimal value of to maximize the applied field during the CQ
  Eddy currents
  L/R time of coil
Luckily, this maximum is occurs around the of TCV scenario

## Slide 38: Plasma Current Scan
Increasing the change in current during the triggered CQ results in significant improvements to REMC performance

## Slide 39: Plasma Current Scan
Increasing the change in current during the triggered CQ results in significant improvements to REMC performance
  Fields above possible for
As expected, this change in current should be maximized during scenario development
The presence of the REMC is expected to improve both the and

## Slide 40
Introduction
Design
Resistance Scan
Scenario Scan
Position Scan
Conclusions and Future Work
OUTLINE

## Slide 41: Plasma Position
Shaped tokamak plasmas are susceptible to vertical displacement events during the CQ
  TCV shape control may allow this to be explored in an experiment
ThinCurr was used to explore the effect of the plasma vertical position on the effectiveness of the REMC
Plasma modeled as a circle with a flat current-profile
  Total plasma current matched to experimentally measured value
  Cross-section area designed to roughly match the experimental scenario

## Slide 42: REMC Performance Sharply Drops off with Vertical Position
Induced current and radial field drop off rapidly with vertical height
The vertical field increases as the plasma approaches the horizontal legs
  Maximized at Z=20cm
    Above this height, performance degrades for all parameters
If VDEs are likely, there is an advantage to tall coils
  As seen for SPARC (Battey et al 2024 Nucl. Fusion)
  Tradeoff with overall less coupled current

## Slide 43
Introduction
Design
Resistance Scan
Scenario Scan
Position Scan
Conclusions and Future Work
OUTLINE

## Slide 44: Conclusions
REMC is currently being designed for TCV
  Installation planned for later this year
Coils are being modeled using a combination of ThinCurr and MARS-Q
  ThinCurr is used to evaluate induced current and vacuum field
  MARS-Q will study driven MHD and RE deconfinement
Keeping the resistivity low will be crucial to the success of the coil
  Maximizing cross-section where possible
  Exploring low-resistivity joint options (polished silver/gold contacts)

## Slide 45: Conclusions
Simulations also indicate the potential for significant coil performance with improvements to the TCV RE scenario
ThinCurr simulations indicate that coils with a vertical height above ~60cm will not couple to sufficient current
Similar to issues predicted for similar midplane coils (DIII-D), the performance of the TCV REMC will fall off steeply at positions above its vertical height

## Slide 46: Thank you
Alex Battey
Postdoctoral Researcher

## Slide 47
Bonus Slides

## Slide 48: REMC Performance Sharply Drops off with Vertical Position

## Slide 49: REMC Performance Sharply Drops off with Vertical Position

## Slide 50: Current Quench Time Scan
Example of fast CQ