## Slide 1: Energy Balance of the Final Collapse in the Runaway Electron Benign Termination Scenario
M. Pedrini ,U. Sheikh, L. Simons, H. Reimerdes, B. Duval, C.Heiss, A. Bettley, E. Tonello, G. Van Parys and the TCV team
Joint Runaway Electron Modelling (REM) and WPTE RT03 Analysis meeting June 2-6 2025, Lausanne
Y. Poels

## Slide 2: Motivation
Assess damage risk via complete energy balance analysis
Support validation of RE mitigation strategies
Estimate the total energy content of the RE beam
Use diagnostics to benchmark all major energy sinks
Understand how RE and plasma energy redistribute at collapse
Notes: Why it's important:
It provides a clean and measurable platform to study the final collapse without complex mitigation artifacts.
It allows energy balance closure, which is hard to achieve in fast disruptions.
It offers unique insights into energy redistribution, especially spatial energy deposition in PFCs and the role of radiative vs. conductive losses.
In the big picture:
Complements high-current device studies (e.g., JET, DIII-D) by providing granular diagnostic access in a smaller tokamak (TCV).
Supplies benchmark data for validating RE modeling codes (e.g., GEANT4, GO, LUKE).
Directly supports ITER-scale mitigation planning by quantifying worst-case energy deposition and by testing diagnostic tools and modeling frameworks.

## Slide 3: Experimental Timing - Final Collapse
Beam creation
  Neon MGI + D2 MGI
Stable RE beam
Compression: Plasma shifted to HFS
  𝑞edge​ reduced until…
MHD instability disruption
  Current quench
  REs are expelled – Final Collapse
Final collapse
Notes: controlled and non-damaging loss of runaway electrons (REs) by ensuring that their energy is dissipated in a way that minimizes localized heat loads on plasma-facing components (PFCs).
Pre-disruption phase – The plasma starts in a normal elongated configuration.
Gas injection (GI) triggers a disruption – A small amount of noble gas (e.g., Ar, Ne) is injected, cooling the plasma and causing a current quench.
Electric field spike accelerates seed electrons – The sudden drop in plasma conductivity induces a strong toroidal electric field, accelerating seed electrons into the runaway regime.
Avalanche multiplication forms the RE beam – Secondary generation dominates, leading to an RE plateau.
Massive gas injection (MGI) introduces low-Z impurities – A second, large gas injection (e.g., D₂, He) increases plasma density and collisionality, slowing down RE acceleration.
A companion plasma forms – The injected gas ionizes and creates a cold, dense plasma coexisting with the RE beam.
Benign termination process begins – The RE beam gradually loses energy via radiation, collisions, and interaction with the companion plasma.
Final collapse expels remaining REs – MHD instabilities grow, leading to RE loss through radiation and wall interactions.

## Slide 4: Energy Balance
Lehnen et al. (2013). Impact and mitigation of disruptions with the ITER-like wall in JET. Nuclear Fusion, 53(9).
Pre collapse available stored energy
Energy sinks during final collapse
?
thermal energy of Companion Plasma
kinetic energy of the RE beam
magnetic energy
radiated energy
energy coupled to machine structures
energy deposited on PFCs

## Slide 5: Magnetic energy Wmag
Wmag estimates from equilibrium reconstructions are unreliable with RE beam
  Key assumptions are violated
Wmag estimated via current ramp experiments
  Assuming Lp and Rp stay constant
  n : time index for instants of the ramps
@ Ip = 150 kA  Wmag = 12 kJ
Notes: LIUQE equilibrium reconstructions are unreliable with RE-dominated plasmas
Standard assumptions in LIUQE break down in presence of RE beam
RE presence violates key assumptions (e.g. isotropic pressure, thermal current)
Magnetic energy estimated via current ramp-down experiments
Assuming constant L<sub>p</sub> and R<sub>p</sub> → W<sub>mag</sub> ≈ 12 kJ at I<sub>p</sub> = 150 kA

## Slide 6: Radiated Energy - Wrad
AXUV diode signal gives precise timing information
Foil bolometers give calibrated Prad measurment
Strong dependence on pre-collapse density [1]
Wrad ~ 5 – 20 kJ
[1] Sheikh, et al(2023). Plasma Physics and Controlled Fusion, 4312.

## Slide 7
Coupled Energy - Wcoupled
Estimated using ThinCurr modeling of currents in vessel structures [2]
  Input : CQ Time, Beam shape from equilibrium reconstruction
Mainly dependent on current quench rates
Estimates for an average CQ ~ 0.5 ms
Wcoupled ~ 4 kJ
[2] Battey, A. et al (2024) Nuclear Fusion, 1(16010).

## Slide 8: Wcond - Energy Deposition on PFCs
Infrared (IR) cameras measure precise surface temperature and wetted area
  Synchrotron  no standard heat flux postprocessing possible
  Toroidal symmetry (sectors 7 and 12 of 16 )  same heat deposition
Pre collapse
Post collapse

## Slide 9: Wcond - Energy Deposition on PFCs
Calorimetry from thermocouples gives total deposited energy
  Confirms toroidal symmetry (sector 7 and 14)
  Analyzed together with IR data
  32 tiles toroidally Wcond = 5 - 20 kJ

## Slide 10: Kinetic energy of the REs- Wkin
Assuming monoenergetic beam and Ip carried fully by the RE beam
Strong dependence on plasma area and volume
  LIUQE equilibrium geometry considered reliable for beam shape estimation
  ERE = 2- 4 MeV
  Wkin = 12-20 kJ

## Slide 11: Heating depth of PFCs
Goal: estimate energy penetration depth into graphite tiles
Combining information on
  IR thermography: surface temperature and wetted area
  Calorimetry: total deposited energy
Assuming uniform heating (tile at IR surface temperature)
   required depth up to 6 mm.
From calorimetry
From IR
h: deposition depth d: graphite density
A: wetted area cp: heat capacity of graphite

## Slide 12: Heating depth of PFCs - GEANT4
Simulated Monoenergetic beams E = 0.2 to 10 MeV
Magnetic field set as in pre-collapse equilibrium
  incoming RE energy is trapped inside the tile
Most energy is deposited very close to the surface
RE penetration depth into graphite (TCV tiles)
  TCV tile ~ 20mm depth

## Slide 13: Conclusions
Comprehensive energy balance reconstructed for the final collapse of RE beams
Initial available energy estimated
Energy losses channels tracked
Simulations with GEANT4 show consistent results with calorimetry and IR cameras
Trustable approach for interpreting RE termination and validate mitigation strategies

## Slide 15: Heat deposition Pattern

## Slide 16: Wcond - Toroidal Symmetry
Infrared (IR) cameras measure precise surface temperature and wetted area
  Synchrotron  no standard heat flux postprocessing possible
  Toroidal symmetry (sectors 7 and 12)  same heat deposition