## Slide 1: 3D MHD simulations of benign terminations of runaway electrons on TCV
Joint REM and WPTE RT03 Analysis meeting, June 2026
Chizhou WANG1,a, Mengdi KONG1, Umar SHEIKH1, Elena TONELLO1, Vinodh BANDARU2, Jonathan GRAVES1, Matthias HOELZL3, the TCV team*, and the JOREK team**
a Email: Chizhou.wang@epfl.ch
1 Swiss Plasma Center, École Polytechnique Fédérale de Lausanne
2 Indian Institute of Technology
3 Max Planck Institute for Plasma Physics
* See the author list of C. Theiler et al 2026 Nucl. Fusion 66 116007
**See the author list of M. Hoelzl et al 2026 Nucl. Fusion 66 116006

## Slide 2: Outline
Final collapse in low-Z benign terminations
JOREK model with fluid REs and neutrals
Scan over neutral density
Conclusions and outlook

## Slide 3: Background
Previous work focused on ne & Te during compression stage, while the plasma scenario can be very different after RE termination starts
Expected evolution:
  Compression: recombined, low ne plasma (~1d18 m-3) ; Ohmic current ~ 0, low Te (~1 eV)
  MHD-induced RE loss, ohmic current re-induced
  Ohmic heating, neutrals re-ionize, Te and ne go up
  Change in Te and ne may affect MHD and following RE termination
Diagnostics:
  No Te data, as plasma deviates from Thomson laser
  Only rough ne from FIR during CQ
  ne spike observed during RE collapse
Reheating and reionization in RE termination might be important to study low-Z benign termination!

## Slide 4: Simulation setup on JOREK
MHD
  Reduced MHD model, n=1-5 toroidal harmonics
  Equilibrium based on TCV #83517, q95=2, q0=0.87, Ip = 149 kA
  Fixed boundary conditions of ψ
REs
  Fluid RE model [V. Bandaru et al. Phys. Rev. 2019], advection v// = c
  Carrying entire Ip at t=0
  Avalanche source on, other sources off
Neutrals
  Fluid, diffusive transport, DN = 2d4 m2/s
Dissipation terms
  Impurity radiation (nNe,bg=1.5d18 m-3), coronal equilibrium assumption
  Deuterium line radiation
  Plasma parallel conduction (8x107 m2/s)
  Neutral conduction missing in JOREK
Bound e- effect
RE-impact ionization neglected

## Slide 5: Spurious loss of RE fluid
RE loss on closed FSs: spurious loss! [C. Wang et al. NF 2026, submitted]
  Physics: flux along magnetic field
  Computation: flux is along grids -> parallel flux has perp term when grid isn’t parallel with FS
  Strong parallel transport in non-FS-aligned finite-element grids -> spurious radial transport
FS
spurious vperp
‘v//’ along grids
Fluid REs runaway from closed FSs
consequence

## Slide 6: Spurious loss of RE fluid
Kinetic REs?
  Pushed in (R,Z,φ) space. They don’t care about grids.
  Too expensive in computation
FS-aligned grids?
  Hard to extend outside plasma boundary for limiter plasma
  MHD over-stabilized by ideal-wall boundary
FS
spurious vperp
RE fluid’s ‘v//’ along grids
Initial grids v.s. FS-aligned grids
RE PIC along field

## Slide 7: Scan on neutral density
nN0 = [2.6d18, 3d19, 4d20] m-3, corresponding with PN~ [0.015, 0.18, 2] Pa according to SOLPS-ITER
Total deuterium neutral + ion population conserved; nN, ne, Te, REs evolves self-consistently
PN (Pa) | nN0 (m-3) | Te(t=0) | ne(t=0)
0.015 (lower limit) | 2.6d18 | 5 eV | 4d18 m-3 on the axis, 1.5d18 m-3 at LCFS
0.18 (benign range) | 3.0d19 | 1.8 eV | 
2 (upper limit) | 4d20 | 0.5 eV | 
Initial condition
PN (Pa) | ne (m-3) simulations/exp | Te(simulations) | RE quench time
0.015 (lower limit) | ~1d19 / 6d19 | > 100 eV | 0.06 ms
0.18 (benign range) | ~1d20 / 2d20 | 30 eV, higher after termination | 0.1 ms
2 (upper limit) | ~2d20 / 3d20 | 2.5 eV, increasing | > 0.1 ms
During early CQ (Before REs are completely lost)
JOREK evolves, MHD grows, RE lost, Te increases, neutrals re-ionize …

## Slide 8: Mode energy growth and IRE decay
Consistent with experiments
  Strong reheating under low nN.
  Low mode amplitude under high nN & ne, probably the result of a growing q95
Deviation from experiments
  Mode amplitude/growth rate under lower limit nN is similar to those in benign range, despite reheating
  Magnetic perturbation one order of magnitude smaller, probably due to the ideal boundary near plasma
Reference from TCV:
in benign cases
under low pressure
under high pressure
q0
q95

## Slide 9: RE evolution
Fast RE deconfinement in low and benign-range nN under low dB: spurious loss!
  Poincare plots from particle tracing at IRE = 130 kA: IRE loss w/o magnetic stochasticity
  Poincare plots at IRE = 20 kA: τloss=L/c up to 1 ms, >> RE fluid quench time
  Experiments: fast RE deconfinement at very early stage of CQ (ΔIp<3%) under much larger dBp
High nN case: nonbenign-like slow RE quench, due to smaller dBp and strong re-avalanche ( > 1020 m-3/s), though spurious loss remains severe
2.6d18
3d19
2.6d18
3d19

## Slide 10: CQ and Energy dissipation
Summary: overestimated RE loss + underestimated radiation power
Pressure | τCQ in experiment | JOREK CQ rate
High | 2-30 ms (IRE dominates) | Over-estimated (large Iohm)
Low/benign range | ~ 1 ms (Ohmic) | Under-estimated (Te too high)
Wrad ~ Wmag in TCV benign cases, but Prad + Pioniz < Pohm in corresponding JOREK simulation
Is coronal equilibrium valid here?
Pioniz << Pohm in low pressure cases
Ip[kA]

## Slide 11: Summary
Lower saturated mode amplitude and strong RE avalanche under high nN, resulting in slow RE termination under high neutral pressure (>1 Pa)
Strong reheating under low nN, but no expected weaker MHD activity
Problems
  Strong spurious numerical RE fluid loss due to non-field-aligned grids
  Magnetic perturbation one order of magnitude smaller than experiments, probably due to fixed boundary close to the plasma
  Weaker radiation than experiments in CQ

## Slide 12: Next step
Construct field-aligned grids for the limiter plasma with the fixed boundary on TCV FW, or apply free boundary condition
Scan nNe to match Wrad in experiments
  Neutral impurities over the whole vessel might flow into plasma during re-ionization, like deuterium does.
Maybe kinetic REs? [Hannes Bergström, et al. PPCF 2025]
Try to explain the physics behind weak MHD under high nN
Study the RE load on the FW by particle tracing

## Slide 13: Thank you for your attention!

## Slide 14: Fluid model of neutrals in JOREK
plasma
neutrals
REs
Iohm/IRE conversion;
RE-MHD interaction
Avalanche source / MHD-induced loss
e-/ion pool;
radiation source
Heated, ionize/recombine
Bound e- boost avalanche
RE impact ionization
(missing in JOREK)
Fluid neutral model in JOREK
  Diffusive transport, DN = 2d4 m2/s
Dissipation terms
  Impurity radiation (nNe,bg=1.5d18 m-3) coronal equilibrium assumption
  Deuterium line radiation
  Plasma parallel conduction (8x107 m2/s)
  Neutral conduction (missing in JOREK)

## Slide 15: Scan on constant and homogeneous ne & Te
High ne (>1d20 m-3) -> slower mode growth, lower saturated energy, upper-limit pressure case better explained?